## Slide 1
Sub-THz
atmospheric sensing
What worked, how we achieved it, and what remains unresolved
Guillem Moreno Garcia
Universitat Politècnica de Catalunya
Supervisor research review · 27 September 2026
Notes: This review describes the research snapshot at commit 461a3ba. Sensing performance remains conditional simulation. The original proposal contains eleven numbered subtasks.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/I2R_proposal_THz_ISAC%20(1).pdf
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 2
Problem statement
Parameter / check | Value
Frequency scope | 60–400 GHz
Satellite altitude | 550 km
Current outputs | 5 VOCs + 3 PM
Family false alarms | 1% budget
Can a satellite communication downlink also detect gas and particle concentration changes using the same transmitted signal?
The proposal covers 60–400 GHz. Gas rotational lines provide spectral structure. Small particles produce a much smoother extinction signature.
The intended outcome combines useful recall, defensible concentration limits and an acceptable communication cost.
The practical question is whether pollutant information survives the other unknowns.
A correct forward model alone does not establish a useful environmental sensor.
02
Notes: LaTeX equation source
\underbrace{\mathbf a}_{\text{observation}}=\underbrace{\mathbf D\mathbf c}_{\text{pollutants}}+\underbrace{\mathbf N\boldsymbol\beta}_{\text{background and instrument}}+\underbrace{\mathbf e}_{\text{noise}}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/I2R_proposal_THz_ISAC%20(1).pdf
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 3
What we have achieved
A completed computational assessment with a conditional VOC improvement
Achievement | Evidence | Boundary
Physical model | Layered gas, particle, ray and thermal calculations | Conditional atmospheric and material assumptions
VOC detection | CH₃CN recall 97.67% at 1 µg/m³ | 20 s total and assumed 0.0001 dB residual
Engineering comparison | Sequential bands and moving coded-frame controls | RF specifications remain unmeasured
Failure diagnosis | PM information, gain drift and communication cost quantified | Useful joint VOC/PM retrieval remains open
CH₃CN interval
97.36–97.96%
Family false alarms
0.79%
Band-selection gain
40.27 percentage points
The 97.67% result uses the selected five-gas design with matched reference weather, 45° elevation, 23 dBm and 6 dB noise figure.
03
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. 10,000 positive trials and 10,000 null trials. Exact recall interval 97.355–97.957%. Family false alarms 0.79%. All five gases and two PM masses remain unknown.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 4
The original eleven tasks
Task | Original requirement | Current outcome
1.1 | Stratified atmosphere | Implemented with standard and measured weather
1.2 | Spectroscopic inputs | Five target VOCs and traceable catalog gaps
1.3 | Line shape and slant integration | Voigt profiles and refracted spherical paths
1.4 | Particle extinction baseline | Rayleigh and Mie models, negative retrieval finding
2.1 | Link and radio parameters | Explicit sequential receiver and resource budget
2.2 | Simulated CSI | AWGN and bounded moving waveform controls
3.1 | Spectral separation | Joint inference with nuisance projection
3.2 | Concentration inversion | Payload moments and signed statistical estimates
4.1 | Variance lower bounds | Nuisance-aware likelihood and Fisher bounds
4.2 | Sensitivity | Common VOC/PM multivariable comparisons
4.3 | Detection floors and standards | Conditional limits, no positive compliance claim
Physical subtasks
4
Radio subtasks
2
Inversion subtasks
2
Performance subtasks
3
04
Notes: Each numbered task receives method and result slides. Task 3.2 lists statistical, optimization and ML methods as alternatives. A neural network is not a mandatory missing requirement.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/I2R_proposal_THz_ISAC%20(1).pdf
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 5
Evidence and operating conditions
Evidence | What it supports | What it cannot establish
HITRAN / ITU models | External physical parameters | Measured atmospheric radio performance
NOAA weather soundings | Actual weather profiles at selected times | Paired VOC/PM concentration truth
Monte Carlo responses | Conditional recall and concentration errors | Field recall under unknown model error
Raw coded OFDM frames | Bounded modem and synchronization checks | Full mission or continuous trajectory validation
Public water / calcite data | Limited independent physical checks | Calibrated joint VOC and PM retrieval
Trials per class
10,000
Current MC cases
12
Reference / sample
10 s / 10 s at 20 s
Measured field recall
Unavailable
Every favorable result needs its time, calibration, concentration and receiver assumptions.
05
Notes: Default current comparison: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. Calibration standard deviation denotes an additional differential spectral residual after reference subtraction. Zero residual is ideal. Nonzero residuals are also unmeasured assumptions.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 6
Task 1.1 · Stratified atmosphere
Parameter / check | Value
Soundings parsed | 521
Vertical levels | 103,322
Gas scale height | 1,500 m
PM scale height | 1,000 m
Implemented ITU-R P.835 reference layers through 100 km and NOAA IGRA measured weather profiles.
Interpolated temperature and log pressure / water vapor across height. Explicitly modeled the continuation above each sounding.
nₛ is molecular number density. Use consistent mass units for cₛ,₀ and molar mass Mₛ. Hₛ is an assumed concentration scale height.
The channel responds to vertical weather variation instead of using one homogeneous slab.
The assumed pollutant profile does not become measured truth because the weather profile is measured.
06
Notes: LaTeX equation source
\begin{aligned}n_s(z)&=\frac{c_{s,0}N_A}{M_s}\exp\!\left(-\frac{z}{H_s}\right),\\[4pt] \text{local spectrum}&\;\text{depends on }P(z),\;T(z),\;\rho_{\mathrm{H_2O}}(z)\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/src/thz_isac/atmosphere.py
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 7
Task 1.1 · Results and profile uncertainty
Component | Implemented result | Remaining uncertainty
Weather archive | 103,322 levels from 521 soundings | Only selected dates enter sensing comparisons
Seasonal cases | January, April, July and September examples | Four profiles do not describe a population
Measured profile tops | 28.8–37.0 km above the station | Upper continuation follows a model
Gas / PM scale height | 1,500 m / 1,000 m | Unknown real pollutant distributions
The reported concentration is a surface-equivalent enhancement under the chosen profile.
Atmosphere top
100 km
Earlier weather cases
4 months
Newest exact grid
2 atmospheres
Absolute ground concentration still requires baseline abundance and a validated column-to-surface mapping.
07
Notes: The newest exact receiver comparison uses standard atmosphere and the existing January sounding. Older broader sensitivity studies include the other months. Do not imply that all four profiles enter the newest 288-condition grid.
LaTeX equation source
c(z)=c_0\exp\!\left(-\frac{z}{H}\right)\qquad\Longrightarrow\qquad\widehat c_0\text{ depends on the assumed }H
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 8
Task 1.2 · Spectroscopic extraction
Parameter / check | Value
Current target gases | 5
Interfering gases | 4
Historical isotope tables | 34
Historical 60–400 GHz lines | 31,474
Acquired line positions, strengths, pressure shifts, air broadening and temperature exponents from HITRAN.
Used isotope-specific masses and partition functions. Preserved line-source hashes and failed acquisition requests.
σₛ is molecular cross section. Sℓ is line strength and Vℓ is the normalized Voigt profile for local temperature and pressure.
The joint receiver now includes five organic gas targets and four interfering gases.
HITRAN strengths already include natural isotope abundance. Applying it twice would understate absorption.
08
Notes: Voigt Doppler width uses isotope mass. Reported mass concentration uses the natural-mixture molar mass. HCOOH rotational intensities involve dipole-based calculations and do not remove spectroscopy uncertainty.
LaTeX equation source
\sigma_s(\nu,z)=\sum_{\ell\in s}S_\ell\!\left(T(z)\right)\,V_\ell\!\left[\nu-\nu_\ell-\delta_\ell P(z);\,T(z),P(z)\right]
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://hitran.org/media/refs/HITRAN-2024.pdf
https://www.hitran.org/docs/molec-meta/
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 9
Task 1.2 · Every target gas and catalog gap
CO, O₃, SO₂ and NO₂ enter as interferents. H₂O and O₂ enter the atmospheric background.
Target | Chemical identity | Current sensing result
H₂CO | Formaldehyde, an aldehyde | Weak recall at 1 µg/m³
CH₃OH | Methanol, an alcohol | Weak recall at 1 µg/m³
CH₃CN | Acetonitrile, a nitrile | Strongest low-concentration candidate
CH₃Cl | Chloromethane, a halogenated gas | Improves at higher concentration
HCOOH | Formic acid, a carboxylic acid | Largest current 95% concentration limit
Formaldehyde 95% limit
7.846 µg/m³
Acetonitrile 95% limit
0.927 µg/m³
Formic acid 95% limit
30.550 µg/m³
CH₃Br, C₂H₄, CH₃F and CH₃I lack suitable lines in the acquired HITRAN window. This does not prove zero absorption.
09
Notes: VOC is the project shorthand for these selected organic gases, not a universal regulatory classification. The retained coverage review uses HITRAN2024 Table 1, page 7. Additional candidates need usable microwave strengths and pressure broadening before quantitative inference.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/missing_spectroscopy_review.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 10
Task 1.3 · Voigt profiles and slant propagation
Parameter / check | Value
Current elevations | 30°, 45°, 60°, 90°
Numerical tolerance | 0.1% RMS
Gas convergence | 0.00381% RMS
Background convergence | 0.00200% RMS
Combined Doppler and pressure broadening at each atmospheric layer.
Integrated along a spherical refracted ray connecting receiver and satellite. Used atmospheric interfaces and numerical quadrature.
A is power attenuation in dB. b is the spherical ray invariant and ζ is the local zenith angle.
Elevation changes both the optical path and the received SNR.
A secant factor applied after vertical integration cannot represent all refracted path effects.
10
Notes: LaTeX equation source
\begin{aligned}A_s(\nu)&=\frac{10}{\ln 10}\int_{\mathrm{ray}}n_s(z)\,\sigma_s(\nu,z)\,\mathrm ds,\\[4pt]\frac{P_{\mathrm{out}}}{P_{\mathrm{in}}}&=10^{-A/10},\qquad b=n(r)\,r\sin\zeta\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 11
Task 1.3 · Numerical convergence and thermal correction
Quantity | Relative RMS difference | Interpretation
Gas integration | 0.00381% | Below the declared 0.1% numerical tolerance
PM integration | 0.0225% | Below the declared tolerance
Atmospheric background | 0.00200% | Below the declared tolerance
Thermal calculation, initial | 0.11596% | Failed and triggered refinement
Thermal calculation, refined | 0.00319% | Passed without relaxing the tolerance
Layer emission contributes receiver noise as well as attenuation.
Lower-atmosphere refinement
100 m steps
Above 20 km
500 m steps
Separate September check
0.05304% RMS
These are numerical checks on the tested grid. They do not measure atmospheric model error.
11
Notes: An independent recursive transfer reproduced the refined brightness. Earlier seasonal weather calculations use order two and only September has its own separate order check. Current selected-tone calculations inherit declared quadrature. Do not claim convergence for every possible weather realization.
LaTeX equation source
T_{\mathrm{sky}}=\sum_i J_\nu(T_i)\left(1-e^{-\tau_i}\right)e^{-\sum_{j<i}\tau_j}+J_\nu(T_{\mathrm{space}})e^{-\sum_i\tau_i}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/45_payload_bounds_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 12
Task 1.4 · Rayleigh and Mie particle models
Parameter / check | Value
Fine density | 1,500 kg/m³
Coarse density | 1,800 kg/m³
Fine index | 1.5 + 0.01i
Coarse index | 1.53 + 0.01i
Integrated spherical Mie extinction over truncated lognormal particle size distributions and normalized it by dry mass.
Converted aerodynamic size cuts to physical particle dimensions using the assumed density and shape model.
q = (m² − 1)/(m² + 2). k is wave number, m complex refractive index, ρ density and r sphere radius.
Rayleigh and full Mie agree closely in this particle-size and frequency regime.
Material refractive index, shape, composition and humidity response remain assumptions.
12
Notes: LaTeX equation source
\begin{aligned}\kappa_{\mathrm{ext}}&=\frac{\int C_{\mathrm{ext}}(r)\,p(r)\,\mathrm dr}{\int \frac{4\pi}{3}\rho r^3p(r)\,\mathrm dr},\\[4pt]\kappa_{\mathrm{abs}}&\simeq\frac{3k\,\mathrm{Im}(q)}{\rho},\qquad\kappa_{\mathrm{sca}}\simeq\frac{2k^4r^3|q|^2}{\rho}\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 13
Task 1.4 · PM definitions and the negative result
Output | Mass represented | Current result
PM1 | Below 1 µm aerodynamic diameter | Exploratory extra split fails numerical separation
PM2.5 | Fine mass below 2.5 µm | No useful mass retrieval in the tested grid
Coarse PM | Disjoint 2.5–10 µm mass | Nearly collinear with the fine-mode signature
PM10 | Fine plus coarse mass | Includes their covariance, no valid 95% limit
The fine model truncates below 0.03 µm. PM10 includes PM2.5, so they are not disjoint particle populations.
Fine Rayleigh/Mie difference
0.00086% RMS
Coarse difference
0.0201% RMS
Three-bin inverse identity error
0.508, rejected
A gain slope removes much of smooth Rayleigh absorption. Shared scattering shapes leave extremely weak size information.
13
Notes: Fine assumptions: density 1500 kg/m³, median physical size 0.5 µm, geometric spread 1.7, refractive index 1.5 + 0.01i. Coarse: 1800 kg/m³, 4 µm, 1.6, 1.53 + 0.01i. Rayleigh/Mie RMS differences are 0.00086% fine and 0.0201% coarse in the earlier physical check. Three-bin scaled inverse identity error is approximately 0.508 and fails the gate.
LaTeX equation source
\mathrm{Var}(\mathrm{PM}_{10})=\mathrm{Var}(c_{\mathrm{fine}})+\mathrm{Var}(c_{\mathrm{coarse}})+2\,\mathrm{Cov}(c_{\mathrm{fine}},c_{\mathrm{coarse}})
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/48_expanded_voc_pm_and_20s_calibration.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 14
Task 2.1 · Link budget and sequential receiver
Parameter / check | Value
Power / noise figure | 23 dBm / 6 dB
Implementation loss | 5 dB
Instantaneous bandwidth | 16 MHz
Settling per hop | 1 ms
Specified a 550 km downlink, 23 dBm active transmit power, 0.50 / 0.30 m apertures and a nominal 6 dB noise figure.
Replaced the ideal simultaneous broad reference with one RF chain hopping across sixteen 16 MHz blocks within 220–330 GHz.
R is range, F the linear noise factor and Limpl the linear implementation loss. Receiver noise figure enters once.
Each block has sixteen 1 MHz tones. CP, pilots, full frames, reference time and retuning all consume the time budget.
23 dBm across the selected bands and 6 dB receiver noise are unverified RF requirements.
14
Notes: LaTeX equation source
\begin{aligned}P_r(\nu)&=\frac{P_t(\nu)G_t(\nu)G_r(\nu)}{L_{\mathrm{impl}}}\left(\frac{\lambda}{4\pi R}\right)^2 10^{-A(\nu)/10},\\[4pt]\mathrm{SNR}(\nu)&=\frac{P_r(\nu)}{kB\left[T_{\mathrm{sky}}(\nu)+T_0(F-1)\right]}\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/47_receiver_design_and_calibration.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 15
Task 2.1 · Resources and communication cost
Quantity | Current result
Total reference + sample time | 20 s, split equally
Actual frame transmission / retuning | 19.72 s / 0.032 s
Instantaneous bandwidth / RF chains | 16 MHz / one
Selected schedule Gaussian rate | 109.52 Mbit/s
Best tested fixed block Gaussian rate | 128.31 Mbit/s
Rate loss against that fixed block | 14.64%
The comparison uses equal instantaneous bandwidth, power and CP/pilot overhead. Both reference and sample carry payload.
Selected center range
224–318.67 GHz
Pilot / frame symbols
30 / 10,000
CP / useful symbol
1 / 16
Zero architecture cost is not established. Gaussian rate is different from coded QPSK throughput.
15
Notes: Best fixed block among tested candidates is centered at 224 GHz. This is not a global optimum over every possible communications design. The older 1.382% number isolates schedule counts and must not replace the full 14.64% comparison.
LaTeX equation source
\overline R=\sum_b\frac{t_b}{t_{\mathrm{total}}}\sum_{k\in b}\Delta f\log_2\!\left(1+\mathrm{SNR}_k\right)
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/communication_tradeoff.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 16
Task 2.2 · CSI and raw waveform simulation
Parameter / check | Value
Blocks / tones per block | 16 / 16
Frame length | 10,000 symbols
Pilots per frame | 30
Acquisition CFO stress | 100 kHz
Generated complex line-of-sight observations with frequency-dependent attenuation and additive complex Gaussian noise.
Added raw IFFT/CP frames, timing acquisition, Doppler correction, pilot tracking and coded packet checks.
Separate raw frames test modem behavior. Large recall experiments draw joint sample moments and apply nonlinear inversion.
The simulation connects physical channel attenuation to a bounded moving receiver.
The large recall study does not generate every raw waveform sample for every Monte Carlo trial.
16
Notes: LaTeX equation source
\begin{aligned}y_k&=h_kx_k+w_k,\qquad w_k\sim\mathcal{CN}(0,V_k),\\[4pt]x[n]&=\operatorname{IFFT}\{X_k\}\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/scope_boundaries.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 17
Task 2.2 · What the waveform controls establish
Control | Retained result | Boundary
Selected-frequency coverage | 16 fresh raw frames | One frequency spot check per selected block
Timing acquisition | 16 / 16 correct | Bounded integer timing model
Passive sensing | Identical decoded outputs in every case | Comparison uses the same scheduled modem
Coded information errors | 1,391 errors | Across 2,826,240 information bits
Full mission dynamics | Still open | Fractional timing, clock drift and time dilation
Narrowband Doppler correction addresses carrier shift. Wideband time scaling requires additional receiver modeling.
Information bits
2,826,240
Information bit errors
1,391
Raw coded bit error rate
0.0492%
Oscillator noise, pointing, multipath and realistic reference availability remain open.
17
Notes: These spot checks support bounded communication behavior, not a measured field recall or a continuous complete orbital pass. Selected_raw_frames.csv retains packet counts and residual CFO.
LaTeX equation source
f_D\simeq\frac{v_r}{c}\,f_c
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/selected_raw_frames.csv
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/scope_boundaries.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 18
Task 3.1 · Joint spectral isolation
Parameter / check | Value
Unknown target masses | 7
Reported outputs | 8 with PM10
Selected frequencies | 256 tones
Scaled identity tolerance | 10⁻⁵
Fitted all five gas signatures and two PM modes simultaneously.
Whitened the observation covariance and projected out gain offset/slope, atmospheric background and four interfering gases.
D contains target signatures. N contains nuisance signatures. QN spans the whitened nuisance space. An SVD constructs H.
Numerical gates check scaled H D ≈ I and nuisance rejection H N ≈ 0.
No algorithm can separate an arbitrary gain error that occupies the same spectral direction as the pollutant.
18
Notes: LaTeX equation source
\begin{aligned}\mathbf a&=\mathbf D\mathbf c+\mathbf N\boldsymbol\beta+\mathbf e,\qquad\mathbf C=\operatorname{Cov}(\mathbf e),\\[4pt]\mathbf P&=\mathbf I-\mathbf Q_N\mathbf Q_N^{\mathsf T},\qquad\widehat{\mathbf c}=\mathbf H\mathbf a\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/scripts/joint_receiver_support.py
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 19
Task 3.1 · Frequency selection improves five-gas inference
A deterministic coordinate-exchange screen selected sixteen blocks using the standard 45° design case.
The selection optimized the worst relative gas uncertainty while retaining PM and nuisance parameters. Exact tone spectra followed the coarse screen.
CH₃CN at 1 µg/m³ | Uniform bands | Selected bands
Simulated recall | 57.40% | 97.67%
Total acquisition time | 20 s | 20 s
Assumed residual standard deviation | 0.0001 dB | 0.0001 dB
Deterministic starts
3
Selected blocks
16
Improved exact gas limits
5 / 5
All five exact VOC information limits improve relative to the uniform design.
January weather and response draws did not choose bands. Global optimality and unknown-weather robustness remain unproved.
19
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. The fresh uniform control is 57.40%. The historical 56.63% value belongs to an earlier independent simulation. The selected result is a conditional improvement at equal resources.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/selection.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 20
Task 3.2 · Payload moments estimate signal and noise
Parameter / check | Value
Pilot fraction per frame | 0.3%
Payload fraction per frame | 99.7%
Signal moments | Second and fourth
Modulation tested | QPSK
Used the existing constant-modulus QPSK payload instead of discarding most samples and retaining only 30 pilots per 10,000 symbols.
Applied the established M2M4 estimator with a finite-sample correction, then compared sample and reference powers.
S is received signal power. V is noise power. The moments separate signal and noise under the QPSK and Gaussian-noise model.
More existing symbols contribute information without adding sensing transmissions.
Arbitrary QAM, nonlinear distortion or severe intercarrier interference invalidate these simple moments.
20
Notes: M2M4 is established prior work. The contribution is its application, resource accounting and conditional evaluation here. Invalid inversions count as failures. Large experiments use the joint asymptotic distribution of second/fourth sample moments and nonlinear inversion. Raw QPSK controls independently test bounded cases.
LaTeX equation source
\begin{aligned}M_2&=S+V,\qquad M_4=S^2+4SV+2V^2,\\[4pt]S&=\sqrt{2M_2^2-M_4},\qquad A=-10\log_{10}\!\left(\frac{S_{\mathrm{sample}}}{S_{\mathrm{reference}}}\right)\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/42_payload_recall.md
https://arxiv.org/abs/2506.15998
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 21
Task 3.2 · Why payload reuse mattered
Earlier ideal broad reference, three target gases and zero persistent calibration residual
Historical control | Pilots | Payload M2M4 | Reference assumption
CH₃CN, 1 µg/m³, 10 s | 0.460% recall | 99.955% recall | Exactly known reference
CH₃CN, 1 µg/m³, 20 s total | 0.380% recall | 93.800% recall | 10 s independent reference + 10 s sample
Pilot samples per frame
30
Total symbols per frame
10,000
Old physical architecture
Ideal simultaneous broad bands
Payload moments recover information that sparse pilot-only sensing discards.
The ideal broad architecture and zero residual assumption prevent direct transfer to deployed hardware.
21
Notes: Historical results in docs/42_payload_recall.md. This table compares methods within each original control. It is separate from the current five-gas hopping receiver and its eight-output false-alarm family. M2M4 itself is established prior work.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/42_payload_recall.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/46_critical_calibration_assumption.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 22
Task 3.2 · Detection gains are species dependent
20 s total, assumed 0.0001 dB residual, selected bands and standard atmosphere at 45°
Gas | Recall at 1 (%) | Misses at 1 (%) | c95 µg/m³ | Recall at c95 (%) | 95% CI at c95 (%) | RMSE at c95 (%)
Formaldehyde | 0.77 | 99.23 | 7.846 | 95.12 | 94.68–95.53 | 21.14
Methanol | 0.75 | 99.25 | 8.838 | 95.12 | 94.68–95.53 | 21.24
Acetonitrile | 97.67 | 2.33 | 0.927 | 95.12 | 94.68–95.53 | 21.49
Chloromethane | 3.58 | 96.42 | 3.918 | 94.72 | 94.26–95.15 | 21.64
Formic acid | 0.16 | 99.84 | 30.550 | 94.85 | 94.40–95.28 | 21.55
Positive / null trials
10,000 / 10,000
Family false alarms
0.79%
Relative RMSE at 95% points
Approximately 21%
Acetonitrile reaches 97.67% recall at 1 µg/m³. Other gases require higher concentrations.
These are simulated detection frequencies, not measured field performance or concentration accuracy.
22
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. Each positive and null class has 10,000 trials. Exact CH3CN interval 97.355–97.957%. Family false alarms 0.79%. At nominal 95% detection points relative concentration RMSE is about 21%, not 5%.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/response_metrics.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 23
Task 4.1 · Lower bounds with nuisance parameters
Parameter / check | Value
Likelihoods | QPSK and magnitude
Unknown noise | Included
Finite reference | Included
Historical efficiency | 95.89–97.61%
Derived full QPSK and magnitude likelihood information with unknown signal power, noise power and finite reference uncertainty.
Profiled nuisance parameters before comparing the attainable concentration covariance with the estimator variance.
c denotes target concentration and η all nuisance parameters. The Schur complement accounts for their uncertainty.
The bound identifies when replacing the estimator offers little remaining gain.
The bound is local and conditional on the likelihood, covariance and physical signatures.
23
Notes: LaTeX equation source
\begin{aligned}J_{ab}&=\mathbb E\!\left[\frac{\partial\log p(y;\boldsymbol\theta)}{\partial\theta_a}\frac{\partial\log p(y;\boldsymbol\theta)}{\partial\theta_b}\right],\\[4pt]\mathbf J_{\mathrm{eff}}&=\mathbf J_{cc}-\mathbf J_{c\eta}\mathbf J_{\eta\eta}^{-1}\mathbf J_{\eta c},\qquad\operatorname{Cov}(\widehat{\mathbf c})\succeq\mathbf J_{\mathrm{eff}}^{-1}\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/44_payload_information_derivation.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/45_payload_bounds_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 24
Task 4.1 · M2M4 is already close to the bound
Historical broad reference, three target gases, 20 s total and zero extra calibration residual
Gas | CRLB / M2M4 variance | Historical 95% limit µg/m³
Formaldehyde | 95.89% | 4.456
Methanol | 97.61% | 10.307
Acetonitrile | 96.49% | 1.023
Values near 100% leave little improvement available from estimator replacement in this control.
Historical output family
6
Acquisition split
10 s + 10 s
Calibration benchmark
Zero extra residual
The next substantial improvement came from frequency information and design.
These historical bounds use a different architecture and target family from the current five-gas receiver.
24
Notes: Standard atmosphere at 45°, charged 10 s reference plus 10 s sample, unknown noise and joint spectral nuisance. The prior six-output family differs from the current eight-output family. Do not use this table to rank current and old designs as equal conditions.
LaTeX equation source
\mathrm{Efficiency}=\frac{\text{variance lower bound}}{\text{estimator variance}}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/45_payload_bounds_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 25
Task 4.2 · Time and calibration jointly set uncertainty
Parameter / check | Value
Time grid | 2 / 20 / 100 s
Residual grid | 0 / 0.0001 / 0.001 dB
Noise-figure grid | 6 / 17 dB
Calibration draws | Once per acquisition
Recomputed the link, absorption, emission and target fit when weather, elevation, bands or receiver noise change.
The latest common grid contains every VOC, PM2.5, coarse PM and PM10 in every operating condition.
Thermal variance decreases with retained symbols. The additional calibration residual persists through the acquisition.
More time helps until persistent calibration error dominates.
The 10 GHz correlation length and each calibration standard deviation remain unmeasured assumptions.
25
Notes: LaTeX equation source
\begin{aligned}\mathbf C(t,\sigma_{\mathrm{cal}})&=\operatorname{diag}\!\left[\mathbf V_{\mathrm{sample}}(t/2)+\mathbf V_{\mathrm{reference}}(t/2)\right]+\sigma_{\mathrm{cal}}^2\mathbf K,\\[4pt]K_{ij}&=\exp\!\left(-\frac{|\nu_i-\nu_j|}{10\,\mathrm{GHz}}\right)\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/global_comparison_protocol.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 26
Task 4.2 · Longer time cannot remove calibration error
Acetonitrile at 1 µg/m³, selected bands, standard atmosphere at 45°
Chart: Simulated recall (%)
| 2 s | 20 s | 100 s
0 dB | 7.58 | 99.28 | 100
0.0001 dB | 7.6 | 97.67 | 100
0.001 dB | 2.24 | 4.36 | 5.05
Parameter / check | Value
20 s, 0 dB | 99.28% recall
20 s, 0.0001 dB | 97.67% recall
20 s, 0.001 dB | 4.36% recall
100 s, 0.001 dB | 5.05% recall
At 0.001 dB, recall is only 4.36% at 20 s and 5.05% at 100 s.
Zero and nonzero residuals are sensitivity assumptions. No receiver stability measurement establishes them.
26
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. Curves use separate finite Monte Carlo samples. The 100% observed values retain confidence intervals below perfect population recall. The covariance is persistent within each acquisition.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/response_metrics.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 27
Task 4.2 · PM shares the full global comparison
Variable | Compared settings
Frequency plan | Uniform and selected sixteen-block schedules
Atmosphere | Standard and January sounding
Elevation | 30°, 45°, 60°, 90°
Reference + sample time | 2 s, 20 s, 100 s
Assumed calibration residual | 0, 0.0001, 0.001 dB
Receiver noise figure | 6 dB and 17 dB
Common result rows
2,304
Rejected settings
Standard, 30°, NF 17 dB
PM predicted recall
Approximately 0.125%
288 conditions × 8 outputs = 2,304 rows. Each output has 270 computed and 18 rejected conditions.
No valid 95% response limit for PM2.5 or PM10 anywhere in this grid.
27
Notes: Fixed 23 dBm transmit power, matched reference weather, 10 GHz residual correlation. All rejected cases are standard atmosphere, 30° elevation, 17 dB noise figure for both schedules and all times/calibrations. Their target separation fails the numerical gate. Failed rows remain present and do not receive fabricated zero recall.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/global_comparison.csv
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/global_comparison_protocol.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 28
Task 4.3 · Detection limits and percentage definitions
Parameter / check | Value
One-sided target α | 0.01 / 8 = 0.00125
Null threshold z | Approximately 3.023
Positive power target | 95%
Absorption cap | 1 dB
Fixed a 1% family false-alarm budget across eight outputs before observing outcomes.
Solved the concentration for nominal 95% power using positive-signal variance, then tested it with fresh simulated responses.
Positive absorption changes SNR and variance. The solution stays within at most 1 dB added absorption.
Reports include low recalls, missed detections, exact binomial intervals and concentration RMSE.
95% detection power, a 95% confidence interval and 5% concentration error describe different quantities.
28
Notes: Recall = TP/(TP+FN). False alarms = FP/(FP+TN). Relative RMSE = sqrt(mean((estimate−truth)^2))/truth. Precision and F1 use artificial 50% prevalence. A missing in-domain solution remains unavailable. The PM10 output participates in the family although it derives from two masses.
LaTeX equation source
\begin{aligned}z&=\Phi^{-1}\!\left(1-\frac{0.01}{8}\right),\qquad\widehat c_j>z\,s_{\mathrm{null}},\\[4pt]c_{95}&=z\,s_{\mathrm{null}}+1.64485\,s_{\mathrm{positive}}(c_{95})\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/scripts/evaluate_joint_receiver.py
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 29
Task 4.3 · Every 95% limit needs time and calibration
Nominal 95% response concentration in µg/m³, selected bands, standard atmosphere at 45°
Total s | Residual dB | H₂CO | CH₃OH | CH₃CN | CH₃Cl | HCOOH
2 | 0 | 25.778 | 27.695 | 2.917 | 12.206 | 102.781
2 | 0.0001 | 25.862 | 27.911 | 2.938 | 12.309 | 102.894
2 | 0.001 | 33.018 | 44.262 | 4.550 | 19.693 | 113.332
20 | 0 | 7.568 | 8.131 | 0.856 | 3.584 | 30.171
20 | 0.0001 | 7.846 | 8.838 | 0.927 | 3.918 | 30.550
20 | 0.001 | 21.913 | 35.377 | 3.557 | 15.567 | 56.267
100 | 0 | 3.361 | 3.612 | 0.380 | 1.592 | 13.400
100 | 0.0001 | 3.945 | 4.999 | 0.517 | 2.226 | 14.228
100 | 0.001 | 20.826 | 34.603 | 3.468 | 15.192 | 49.310
CH₃CN, 20 s / 0.0001 dB
0.927 µg/m³
CH₃CN, 100 s / 0.001 dB
3.468 µg/m³
Valid PM limits in nine cases
0
PM2.5, coarse PM and PM10 have no valid 95% response limit in these nine conditions.
29
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. Values solve positive-response variance and precede Monte Carlo evaluation. Actual simulated recalls near 95% remain as measured fractions in the response CSV. All calibration levels are assumed.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/response_metrics.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 30
Task 4.3 · Environmental interpretation remains open
Parameter / check | Value
H₂CO current limit ppm | 0.006179
CH₃CN current limit ppm | 0.000534
Limit conditions | 20 s / 0.0001 dB
Ambient PM test masses | 15 and 45 µg/m³
Converted gas mass to surface-equivalent mole fraction using pressure, temperature and molar mass.
Observable: short slant-path enhancement relative to a reference. Ambient guidance has distinct location and averaging requirements.
PM reference masses are 15 and 45 µg/m³. These tests do not establish compliance.
The numeric conversion assumes the displayed mass and molar-mass units. PM has mass units and no gas ppm conversion.
The study reports conditional floors and an explicit negative / unverified standards assessment.
Unknown baseline abundance, vertical profiles, PM information and independent truth prevent a positive compliance claim.
30
Notes: The prior standards review discusses WHO 2021 ambient PM guidelines and separate indoor formaldehyde guidance. These are different domains and time averages. This presentation does not interpret short radio enhancements as regulatory measurements.
LaTeX equation source
\chi_{\mathrm{ppm}}=\frac{c_{\mu\mathrm{g}/\mathrm m^3}\,R\,T}{p\,M_{\mathrm g/\mathrm{mol}}}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/45_payload_bounds_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/41_measurement_protocol.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 31
Calibration is the critical engineering requirement
Parameter / check | Value
Required local σ at 20 s | About 0.000146 dB
Nominal random σ | 0.0001 dB
Power change for 0.0001 dB | About 0.002303%
Field calibration records | None
Zero calibration error means zero additional differential residual after modeled corrections. Thermal noise and reference uncertainty still remain.
At 20 s, the local CH₃CN requirement for 95% power at 1 µg/m³ is approximately 0.000146 dB residual standard deviation under the nominal covariance.
A persistent signed bias can move both the null threshold and the positive response in the adverse direction.
Calibration requirements are now quantitative and retained with every result.
A small random standard deviation does not guarantee resistance to arbitrary drift or unknown hop gains.
31
Notes: The 0.000146 dB number is a local requirement, not a measured achieved accuracy. Independent hop-gain nuisance terms make the current separation unstable. Prior zero-calibration headline controls are retained separately in the permanent calibration note.
LaTeX equation source
\begin{aligned}|b_i|&\leq\varepsilon\quad\Longrightarrow\quad B_j=\varepsilon\,\lVert\mathbf H_j\rVert_1,\\[4pt]c_{95,\mathrm{protected}}&\simeq(z+1.64485)s_j+2B_j\end{aligned}
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/46_critical_calibration_assumption.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/calibration_requirements.csv
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 32
Failures that constrain the claimed achievement
Failure or stress | Finding | Implication
PM mass and extra size split | Negligible useful information / unstable inverse | A successful optimizer cannot repair missing information
Unknown relative hop gains | Target separation fails | Requires calibrated relative spectral response
Weather mismatch | Frozen standard operator acquires bias | Matched-weather success is insufficient
Unamplified RF converter | Fails usable-SNR gate | Nominal power requires a complete RF chain
Modulation / receiver mismatch | Simple payload moments may become invalid | Receiver assumptions need dedicated validation
Numerically rejected global cases
18 / 288
Useful PM limits
0 / 270 valid cases
Gaussian architecture rate loss
14.64%
The intended general atmospheric VOC/PM instrument remains an open research outcome.
32
Notes: All listed failures remain in the current audit and retained stress outputs. The nominal 17 dB noise-figure grid also rejects standard atmosphere at 30° for both schedules. Successful runs do not conceal those cases.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/stress_sensitivity.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 33
Remaining problems and evidence needed
Open problem | Evidence required to close it
RF hardware and calibration | Measured power, noise, settling, spectral covariance and drift at selected tones
PM mass / composition | Paired optical properties, humidity, particle size and independent mass truth
Weather and concentration profiles | Independent profiles, column information and reference abundance
Full receiver dynamics | Continuous time-scaled channel with fractional timing, oscillator and pointing errors
Independent validation | Separate calibration and test campaigns with paired radio / concentration data
Deployment and environmental use | Applicable averaging domain, spectrum coordination and realistic operational coverage
Nominal RF target
23 dBm, NF 6 dB
Current calibration assumption
0.0001 dB
Current physical truth
No paired radio/VOC/PM test
33
Notes: Complete remaining-work ledger: docs/49_completion_audit_and_fixes.md. Additional unresolved details include unequal dwell/global frequency optimization, spectroscopy uncertainty, real-time hardware latency, atmospheric horizontal variability and communication coding/adaptation baselines.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/41_measurement_protocol.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 34
Proposed next experiments
Priority | Experiment | Decision it enables
1 | Repeated blank / reference acquisitions at selected tones | Can the required differential stability be achieved?
2 | Controlled gas path with independent concentration truth | Does the predicted VOC recall survive real model error?
3 | PM cell with known mass, size and humidity | Does radio information separate mass from composition?
4 | Full receiver and reference schedule under motion | Can the sensing result survive operational timing?
Calibration acceptance question
σ ≤ about 0.000146 dB at 20 s?
Frozen test target
1 µg/m³ CH₃CN
Independent test measurements
Still required
Freeze calibration and model choices before evaluating an independent test campaign.
Additional Monte Carlo trials improve numerical precision but cannot replace missing measurements.
34
Notes: These are proposed next experiments. No campaign has been completed or funded by this presentation. Before hardware access, full warped-time simulation and an additional PM observable are the most useful computational follow-ups.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/41_measurement_protocol.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 35
What we can report to the supervisor
Parameter / check | Value
Task implementations | 11 / 11
Verified research checks | 25,172
Conditional CH₃CN recall | 97.67%
Validated field recall | Unavailable
The original eleven modeling and simulation tasks now have implementations with traceable outputs.
Payload reuse and frequency selection improve conditional VOC detection. Acetonitrile reaches 97.67% recall at 1 µg/m³ with 20 s and assumed 0.0001 dB residual.
The analysis explains why PM remains weak and why more averaging cannot overcome persistent calibration error.
The next milestone is independent physical validation of the selected receiver and its concentration estimates.
The main achievement is a reproducible feasibility assessment and a stronger, explicitly conditional VOC design.
Useful joint PM retrieval, zero communication architecture cost and validated field performance remain unachieved.
35
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. The current schedule loses 14.64% Gaussian rate against the best tested fixed block. Source snapshot 461a3ba retains 235 tests and 25,172 numerical checks. These verify implementation and consistency, not physical truth.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 36
Appendix · Global VOC and PM outcomes
Envelopes over 270 valid operating conditions per output, with 18 additional rejected conditions
Output | Reference µg/m³ | Predicted recall range | Valid 95% limits / 270
H2CO | 1 | 0.128–89.043% | 270
CH3OH | 1 | 0.130–72.886% | 270
CH3CN | 1 | 0.282–100.000% | 270
CH3Cl | 1 | 0.139–100.000% | 270
HCOOH | 1 | 0.125–12.651% | 269
PM2.5 | 15 | 0.125–0.125% | 0
PMcoarse | 45 | 0.125–0.125% | 0
PM10 | 45 | 0.125–0.125% | 0
Grid
2 plans × 2 weather × 4 elevations
Other axes
3 times × 3 residuals × 2 noise figures
Mass assumptions
1 / 15 / 45 µg/m³ (see table)
Different reference concentrations and operating conditions prevent a direct same-condition species ranking.
36
Notes: These are conditional predictions using positive-response variance, not Monte Carlo frequencies. Ranges are operating-condition envelopes, not confidence intervals. Full 288-condition axes appear on Task 4.2 slides. Power fixed at 23 dBm and reference weather matched.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/global_comparison.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 37
Appendix · Low PM recalls remain visible
Simulated recall, selected bands, standard atmosphere at 45°, same joint five-gas fit
Total s | Residual dB | PM2.5 at 15 µg/m³ | Coarse at 45 µg/m³ | PM10 at 45 µg/m³
2 | 0 | 0.14% | 0.14% | 0.12%
2 | 0.0001 | 0.10% | 0.10% | 0.06%
2 | 0.001 | 0.09% | 0.11% | 0.14%
20 | 0 | 0.11% | 0.15% | 0.16%
20 | 0.0001 | 0.15% | 0.07% | 0.14%
20 | 0.001 | 0.15% | 0.19% | 0.09%
100 | 0 | 0.15% | 0.12% | 0.10%
100 | 0.0001 | 0.08% | 0.13% | 0.07%
100 | 0.001 | 0.07% | 0.10% | 0.13%
PM10 positive mixture
Fine 49/90, coarse 41/90
Null target threshold
0.125% theoretical marginal rate
Monte Carlo class size
10,000
These recalls are near the false-alarm scale. No cell establishes useful PM detection.
37
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. PM10 positive injection uses fine/coarse fractions 49/90 and 41/90. Each class has 10,000 trials. Binomial variation explains small nonmonotonic differences near the null rate. PM10 variance includes the cross covariance.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/response_metrics.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 38
Appendix · Reproducible evidence map
Research snapshot 461a3ba, 27 September 2026
Research material | Repository location
Original task definition | I2R_proposal_THz_ISAC (1).pdf
Current results and global comparison | docs/51_joint_design_time_calibration_results.md
Species, equations and metric definitions | docs/50_species_methods_and_percentage_guide.md
Complete open-issue ledger | docs/49_completion_audit_and_fixes.md
Critical calibration record | docs/46_critical_calibration_assumption.md
Data, trials, hashes and validation | results/joint_receiver_revision/
Current manuscript | output/pdf/thz_isac_pollutant_sensing_ieee.pdf
Retained metric rows
480
Global rows
2,304
Passing research tests
235
38
Notes: Repository: https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring . The snapshot contains 235 passing tests and 25,172 numerical checks. These counts describe the computational research snapshot, not slide validation or independent physical evidence.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 39
Appendix · Physical and methodological sources
Parameter / check | Value
Original tasks | 11
Current source snapshot | 461a3ba
Additional organic catalog gaps | 4
Paired field validation | Open
HITRAN2024 and HAPI: line data, isotope handling and spectroscopic calculations.
ITU-R P.835 and P.676: reference atmosphere, oxygen/water absorption and atmospheric background.
NOAA IGRA: independent measured weather soundings.
Aliaga et al. (2024) and Yang et al. (2024): satellite differential absorption and gas/particle propagation context.
Xu, Fu and Kim (2025): using pilots and payloads for sensing. Established M2M4 literature supplies the signal/noise estimator.
Published models motivate and parameterize the study. They do not validate this receiver’s field performance.
39
Notes: Sources:
HITRAN2024: https://hitran.org/media/refs/HITRAN-2024.pdf
HAPI: https://doi.org/10.1016/j.jqsrt.2016.03.005
ITU-R P.835-7: https://www.itu.int/rec/R-REC-P.835
ITU-R P.676-13: https://www.itu.int/rec/R-REC-P.676
NOAA IGRA: https://www.ncei.noaa.gov/products/weather-balloon/integrated-global-radiosonde-archive
Aliaga et al.: https://doi.org/10.1109/JSTARS.2024.3480816
Yang et al.: https://doi.org/10.1109/OJCOMS.2024.3386759
Xu et al.: https://arxiv.org/abs/2506.15998
M2M4: Gianmarco Romano, 2021, doi:10.3390/s21154950. See full references in current manuscript.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.