## Slide 1
Sub-THz
atmospheric sensing
What worked, how we achieved it, and what remains unresolved
Guillem Moreno Garcia
Universitat Politècnica de Catalunya
Supervisor research review · 27 September 2026
Notes: This review describes the research snapshot at commit 461a3ba. Sensing performance remains conditional simulation. The original proposal contains eleven numbered subtasks.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/I2R_proposal_THz_ISAC%20(1).pdf
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 2
Problem statement
Parameter / check | Value
Frequency scope | 60–400 GHz
Satellite altitude | 550 km
Current outputs | 5 VOCs + 3 PM
Family false alarms | 1% budget
Can a satellite communication downlink also detect gas and particle concentration changes using the same transmitted signal?
The proposal covers 60–400 GHz. Gas rotational lines provide spectral structure. Small particles produce a much smoother extinction signature.
The intended outcome combines useful recall, defensible concentration limits and an acceptable communication cost.
The practical question is whether pollutant information survives the other unknowns.
A correct forward model alone does not establish a useful environmental sensor.
Notation and units
a: measured attenuation vector (dB)
D: target spectral response matrix
c: target concentrations (µg/m³)
N: background / instrument response matrix
β: nuisance parameter vector
D c and N β: attenuation contributions (dB)
e: measurement error vector (dB)
Bold letters: vectors or matrices
Matrix products sum spectral contributions
02
Notes: LaTeX equation source
\underbrace{\mathbf a}_{\text{observation}}=\underbrace{\mathbf D\mathbf c}_{\text{pollutants}}+\underbrace{\mathbf N\boldsymbol\beta}_{\text{background and instrument}}+\underbrace{\mathbf e}_{\text{noise}}
Notation legend
a: measured attenuation vector (dB)
D: target spectral response matrix
c: target concentrations (µg/m³)
N: background / instrument response matrix
β: nuisance parameter vector
D c and N β: attenuation contributions (dB)
e: measurement error vector (dB)
Bold letters: vectors or matrices
Matrix products sum spectral contributions
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/I2R_proposal_THz_ISAC%20(1).pdf
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 3
What we have achieved
A completed computational assessment with a conditional VOC improvement
Achievement | Evidence | Boundary
Physical model | Layered gas, particle, ray and thermal calculations | Conditional atmospheric and material assumptions
VOC detection | CH₃CN recall 97.67% at 1 µg/m³ | 20 s total and assumed 0.0001 dB residual
Engineering comparison | Sequential bands and moving coded-frame controls | RF specifications remain unmeasured
Failure diagnosis | PM information, gain drift and communication cost quantified | Useful joint VOC/PM retrieval remains open
CH₃CN interval
97.36–97.96%
Family false alarms
0.79%
Band-selection gain
40.27 percentage points
The 97.67% result uses the selected five-gas design with matched reference weather, 45° elevation, 23 dBm and 6 dB noise figure.
03
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. 10,000 positive trials and 10,000 null trials. Exact recall interval 97.355–97.957%. Family false alarms 0.79%. All five gases and two PM masses remain unknown.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 4
The original eleven tasks
Task | Original requirement | Current outcome
1.1 | Stratified atmosphere | Implemented with standard and measured weather
1.2 | Spectroscopic inputs | Five target VOCs and traceable catalog gaps
1.3 | Line shape and slant integration | Voigt profiles and refracted spherical paths
1.4 | Particle extinction baseline | Rayleigh and Mie models, negative retrieval finding
2.1 | Link and radio parameters | Explicit sequential receiver and resource budget
2.2 | Simulated CSI | AWGN and bounded moving waveform controls
3.1 | Spectral separation | Joint inference with nuisance projection
3.2 | Concentration inversion | Payload moments and signed statistical estimates
4.1 | Variance lower bounds | Nuisance-aware likelihood and Fisher bounds
4.2 | Sensitivity | Common VOC/PM multivariable comparisons
4.3 | Detection floors and standards | Conditional limits, no positive compliance claim
Physical subtasks
4
Radio subtasks
2
Inversion subtasks
2
Performance subtasks
3
04
Notes: Each numbered task receives method and result slides. Task 3.2 lists statistical, optimization and ML methods as alternatives. A neural network is not a mandatory missing requirement.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/I2R_proposal_THz_ISAC%20(1).pdf
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 5
Evidence and operating conditions
Each task explains its inputs on the method slide. Detailed dataset records remain on slides 40–44.
Evidence | What it supports | What it cannot establish
HITRAN / ITU models | External physical parameters | Measured atmospheric radio performance
NOAA weather soundings | Actual weather profiles at selected times | Paired VOC/PM concentration truth
Monte Carlo responses | Conditional recall and concentration errors | Field recall under unknown model error
Raw coded OFDM frames | Bounded modem and synchronization checks | Full mission or continuous trajectory validation
Public water / calcite data | Limited independent physical checks | Calibrated joint VOC and PM retrieval
Trials per class
10,000
Current MC cases
12
Reference / sample
10 s / 10 s at 20 s
Measured field recall
Unavailable
Every favorable result needs its time, calibration, concentration and receiver assumptions.
05
Notes: Default current comparison: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. Calibration standard deviation denotes an additional differential spectral residual after reference subtraction. Zero residual is ideal. Nonzero residuals are also unmeasured assumptions.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 6
Task 1.1 · Stratified atmosphere
Parameter / check | Value
Soundings parsed | 521
Vertical levels | 103,322
Gas scale height | 1,500 m
PM scale height | 1,000 m
Implemented ITU-R P.835 reference layers through 100 km and NOAA IGRA measured weather profiles.
Interpolated temperature and log pressure / water vapor across height. Explicitly modeled the continuation above each sounding.
nₛ is molecular number density. Use consistent mass units for cₛ,₀ and molar mass Mₛ. Hₛ is an assumed concentration scale height.
The channel responds to vertical weather variation instead of using one homogeneous slab.
The assumed pollutant profile does not become measured truth because the weather profile is measured.
Data and models used
NOAA IGRA: Beijing CHM00054511.
2026 snapshot: 521 soundings.
1 January profile in the current grid.
Jan/Apr/Jul/Sep in earlier checks.
Used for pressure, T and humidity.
ITU P.835 supplies the standard case.
VOC/PM vertical profiles are assumed.
Notation and units
s: gas species index
z: altitude (m)
n_s(z): molecular number density (m⁻³)
c_s,0: surface mass concentration (kg/m³)
N_A: Avogadro constant (mol⁻¹)
M_s: gas molar mass (kg/mol)
H_s: assumed concentration scale height (m)
exp: exponential function
P(z): atmospheric pressure (Pa)
T(z): atmospheric temperature (K)
ρ_H₂O(z): water vapour mass density (kg/m³)
Convert µg/m³ to kg/m³ before substitution
06
Notes: Data and models used
NOAA IGRA: Beijing CHM00054511.
2026 snapshot: 521 soundings.
1 January profile in the current grid.
Jan/Apr/Jul/Sep in earlier checks.
Used for pressure, T and humidity.
ITU P.835 supplies the standard case.
VOC/PM vertical profiles are assumed.
LaTeX equation source
\begin{aligned}n_s(z)&=\frac{c_{s,0}N_A}{M_s}\exp\!\left(-\frac{z}{H_s}\right),\\[4pt] \text{local spectrum}&\;\text{depends on }P(z),\;T(z),\;\rho_{\mathrm{H_2O}}(z)\end{aligned}
Notation legend
s: gas species index
z: altitude (m)
n_s(z): molecular number density (m⁻³)
c_s,0: surface mass concentration (kg/m³)
N_A: Avogadro constant (mol⁻¹)
M_s: gas molar mass (kg/mol)
H_s: assumed concentration scale height (m)
exp: exponential function
P(z): atmospheric pressure (Pa)
T(z): atmospheric temperature (K)
ρ_H₂O(z): water vapour mass density (kg/m³)
Convert µg/m³ to kg/m³ before substitution
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/src/thz_isac/atmosphere.py
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 7
Task 1.1 · Results and profile uncertainty
Component | Implemented result | Remaining uncertainty
Weather archive | 103,322 levels from 521 soundings | Only selected dates enter sensing comparisons
Seasonal cases | January, April, July and September examples | Four profiles do not describe a population
Measured profile tops | 28.8–37.0 km above the station | Upper continuation follows a model
Gas / PM scale height | 1,500 m / 1,000 m | Unknown real pollutant distributions
The reported concentration is a surface-equivalent enhancement under the chosen profile.
Atmosphere top
100 km
Earlier weather cases
4 months
Newest exact grid
2 atmospheres
Absolute ground concentration still requires baseline abundance and a validated column-to-surface mapping.
Notation and units
c(z): mass concentration at altitude z
c₀: surface mass concentration
c and c₀ use the same mass / volume units
z: altitude (m)
H: assumed concentration scale height (m)
exp: exponential function
ĉ₀: estimated surface mass concentration
Hat: estimated quantity
⇒: implication under the assumed profile
07
Notes: The newest exact receiver comparison uses standard atmosphere and the existing January sounding. Older broader sensitivity studies include the other months. Do not imply that all four profiles enter the newest 288-condition grid.
LaTeX equation source
c(z)=c_0\exp\!\left(-\frac{z}{H}\right)\qquad\Longrightarrow\qquad\widehat c_0\text{ depends on the assumed }H
Notation legend
c(z): mass concentration at altitude z
c₀: surface mass concentration
c and c₀ use the same mass / volume units
z: altitude (m)
H: assumed concentration scale height (m)
exp: exponential function
ĉ₀: estimated surface mass concentration
Hat: estimated quantity
⇒: implication under the assumed profile
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 8
Task 1.2 · Spectroscopic extraction
Parameter / check | Value
Current target gases | 5
Interfering gases | 4
Current isotope tables | 25
Current acquired lines | 319,001
Acquired line positions, strengths, pressure shifts, air broadening and temperature exponents from HITRAN.
Used isotope-specific masses and partition functions. Preserved line-source hashes and failed acquisition requests.
σₛ is molecular cross section. Sℓ is line strength and Vℓ is the normalized Voigt profile for local temperature and pressure.
The joint receiver now includes five organic gas targets and four interfering gases.
HITRAN strengths already include natural isotope abundance. Applying it twice would understate absorption.
Data and models used
HITRAN2024, acquired via HAPI.
319,001 lines, 25 isotope tables.
Acquisition window: 0–3000 GHz.
Five VOC targets + four interferents.
Line strength, width, shift and energy
feed the local absorption profiles.
HAPI supplies masses and partition sums.
Notation and units
s: species index, ℓ: spectral line index
ν: spectral frequency, ν_ℓ: line centre
z: altitude (m)
σ_s: molecular absorption cross section (m²)
S_ℓ(T): integrated line strength at T
V_ℓ: normalized Voigt line profile
S_ℓ × V_ℓ has cross section units
Use matching spectral units for S_ℓ and V_ℓ
T(z): atmospheric temperature (K)
P(z): atmospheric pressure
δ_ℓ: line shift per unit pressure
δ_ℓ P(z): pressure shift in frequency units
08
Notes: Voigt Doppler width uses isotope mass. Reported mass concentration uses the natural-mixture molar mass. HCOOH rotational intensities involve dipole-based calculations and do not remove spectroscopy uncertainty.
Data and models used
HITRAN2024, acquired via HAPI.
319,001 lines, 25 isotope tables.
Acquisition window: 0–3000 GHz.
Five VOC targets + four interferents.
Line strength, width, shift and energy
feed the local absorption profiles.
HAPI supplies masses and partition sums.
LaTeX equation source
\sigma_s(\nu,z)=\sum_{\ell\in s}S_\ell\!\left(T(z)\right)\,V_\ell\!\left[\nu-\nu_\ell-\delta_\ell P(z);\,T(z),P(z)\right]
Notation legend
s: species index, ℓ: spectral line index
ν: spectral frequency, ν_ℓ: line centre
z: altitude (m)
σ_s: molecular absorption cross section (m²)
S_ℓ(T): integrated line strength at T
V_ℓ: normalized Voigt line profile
S_ℓ × V_ℓ has cross section units
Use matching spectral units for S_ℓ and V_ℓ
T(z): atmospheric temperature (K)
P(z): atmospheric pressure
δ_ℓ: line shift per unit pressure
δ_ℓ P(z): pressure shift in frequency units
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://hitran.org/media/refs/HITRAN-2024.pdf
https://www.hitran.org/docs/molec-meta/
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 9
Task 1.2 · Every target gas and catalog gap
CO, O₃, SO₂ and NO₂ enter as interferents. H₂O and O₂ enter the atmospheric background.
Target | Chemical identity | Current sensing result
H₂CO | Formaldehyde, an aldehyde | Weak recall at 1 µg/m³
CH₃OH | Methanol, an alcohol | Weak recall at 1 µg/m³
CH₃CN | Acetonitrile, a nitrile | Strongest low-concentration candidate
CH₃Cl | Chloromethane, a halogenated gas | Improves at higher concentration
HCOOH | Formic acid, a carboxylic acid | Largest current 95% concentration limit
Formaldehyde 95% limit
7.846 µg/m³
Acetonitrile 95% limit
0.927 µg/m³
Formic acid 95% limit
30.550 µg/m³
CH₃Br, C₂H₄, CH₃F and CH₃I lack suitable lines in the acquired HITRAN window. This does not prove zero absorption.
09
Notes: VOC is the project shorthand for these selected organic gases, not a universal regulatory classification. The retained coverage review uses HITRAN2024 Table 1, page 7. Additional candidates need usable microwave strengths and pressure broadening before quantitative inference.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/missing_spectroscopy_review.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 10
Task 1.3 · Voigt profiles and slant propagation
Parameter / check | Value
Current elevations | 30°, 45°, 60°, 90°
Numerical tolerance | 0.1% RMS
Gas convergence | 0.00381% RMS
Background convergence | 0.00200% RMS
Combined Doppler and pressure broadening at each atmospheric layer.
Integrated along a spherical refracted ray connecting receiver and satellite. Used atmospheric interfaces and numerical quadrature.
A is power attenuation in dB. b is the spherical ray invariant and ζ is the local zenith angle.
Elevation changes both the optical path and the received SNR.
A secant factor applied after vertical integration cannot represent all refracted path effects.
Data and models used
HITRAN: the same nine-gas line pool.
ITU P.676: oxygen/water background.
ITU / January IGRA atmospheric states.
Used in layerwise slant integration.
Water paper, Fig. 8, 380.197 GHz:
published slopes are a separate check.
No measured atmospheric THz paths.
Notation and units
s: gas species, ν: frequency
A_s and A: power attenuation (dB)
n_s: molecular number density (m⁻³)
σ_s: molecular cross section (m²)
ds: differential path length along ray (m)
P_in and P_out: input and output power (W)
z: altitude (m)
ln: natural logarithm
b: conserved spherical ray invariant (m)
n(r): refractive index at radial distance r
r: distance from Earth’s centre (m)
ζ: local zenith angle
10
Notes: Data and models used
HITRAN: the same nine-gas line pool.
ITU P.676: oxygen/water background.
ITU / January IGRA atmospheric states.
Used in layerwise slant integration.
Water paper, Fig. 8, 380.197 GHz:
published slopes are a separate check.
No measured atmospheric THz paths.
LaTeX equation source
\begin{aligned}A_s(\nu)&=\frac{10}{\ln 10}\int_{\mathrm{ray}}n_s(z)\,\sigma_s(\nu,z)\,\mathrm ds,\\[4pt]\frac{P_{\mathrm{out}}}{P_{\mathrm{in}}}&=10^{-A/10},\qquad b=n(r)\,r\sin\zeta\end{aligned}
Notation legend
s: gas species, ν: frequency
A_s and A: power attenuation (dB)
n_s: molecular number density (m⁻³)
σ_s: molecular cross section (m²)
ds: differential path length along ray (m)
P_in and P_out: input and output power (W)
z: altitude (m)
ln: natural logarithm
b: conserved spherical ray invariant (m)
n(r): refractive index at radial distance r
r: distance from Earth’s centre (m)
ζ: local zenith angle
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 11
Task 1.3 · Numerical convergence and thermal correction
Quantity | Relative RMS difference | Interpretation
Gas integration | 0.00381% | Below the declared 0.1% numerical tolerance
PM integration | 0.0225% | Below the declared tolerance
Atmospheric background | 0.00200% | Below the declared tolerance
Thermal calculation, initial | 0.11596% | Failed and triggered refinement
Thermal calculation, refined | 0.00319% | Passed without relaxing the tolerance
Layer emission contributes receiver noise as well as attenuation.
Lower-atmosphere refinement
100 m steps
Above 20 km
500 m steps
Separate September check
0.05304% RMS
These are numerical checks on the tested grid. They do not measure atmospheric model error.
Notation and units
T_sky: equivalent sky noise temperature (K)
ν: frequency (Hz)
T_i: physical temperature of layer i (K)
J_ν(T): Planck brightness temperature (K)
τ_i: dimensionless optical depth of layer i
i: emitting layer, j: intervening layer
j < i: layers between layer i and receiver
T_space: space background temperature (K)
exp(−τ): power transmission through a layer
11
Notes: An independent recursive transfer reproduced the refined brightness. Earlier seasonal weather calculations use order two and only September has its own separate order check. Current selected-tone calculations inherit declared quadrature. Do not claim convergence for every possible weather realization.
LaTeX equation source
T_{\mathrm{sky}}=\sum_i J_\nu(T_i)\left(1-e^{-\tau_i}\right)e^{-\sum_{j<i}\tau_j}+J_\nu(T_{\mathrm{space}})e^{-\sum_i\tau_i}
Notation legend
T_sky: equivalent sky noise temperature (K)
ν: frequency (Hz)
T_i: physical temperature of layer i (K)
J_ν(T): Planck brightness temperature (K)
τ_i: dimensionless optical depth of layer i
i: emitting layer, j: intervening layer
j < i: layers between layer i and receiver
T_space: space background temperature (K)
exp(−τ): power transmission through a layer
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/45_payload_bounds_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 12
Task 1.4 · Rayleigh and Mie particle models
Parameter / check | Value
Fine density | 1,500 kg/m³
Coarse density | 1,800 kg/m³
Fine index | 1.5 + 0.01i
Coarse index | 1.53 + 0.01i
Integrated spherical Mie extinction over truncated lognormal particle size distributions and normalized it by dry mass.
Converted aerodynamic size cuts to physical particle dimensions using the assumed density and shape model.
q = (m² − 1)/(m² + 2). k is wave number, m complex refractive index, ρ density and r sphere radius.
Rayleigh and full Mie agree closely in this particle-size and frequency regime.
Material refractive index, shape, composition and humidity response remain assumptions.
Data and models used
Inputs: assumed aerosol properties.
Fine 0.03–2.5 µm; coarse 2.5–10 µm.
Density and refractive index shown above.
Used for mass-normalized extinction.
Calcite: 8 sample + 4 blank recordings.
Separate transmission check only:
no measured PM mass or size labels.
Notation and units
κ_ext, κ_abs, κ_sca: mass coefficients
Extinction, absorption, scattering (m²/kg)
C_ext(r): particle extinction cross section (m²)
p(r): particle number distribution in radius
r: physical particle radius (m)
ρ: particle material density (kg/m³)
k = 2π/λ: electromagnetic wavenumber (m⁻¹)
λ: wavelength in the surrounding medium (m)
q = (m² − 1)/(m² + 2): contrast factor
m: complex relative refractive index
Im(q): imaginary part of q
|q|²: squared complex magnitude
dr: radius integration element (m)
≃: Rayleigh approximation for small particles
The two final terms describe one radius r
12
Notes: Data and models used
Inputs: assumed aerosol properties.
Fine 0.03–2.5 µm; coarse 2.5–10 µm.
Density and refractive index shown above.
Used for mass-normalized extinction.
Calcite: 8 sample + 4 blank recordings.
Separate transmission check only:
no measured PM mass or size labels.
LaTeX equation source
\begin{aligned}\kappa_{\mathrm{ext}}&=\frac{\int C_{\mathrm{ext}}(r)\,p(r)\,\mathrm dr}{\int \frac{4\pi}{3}\rho r^3p(r)\,\mathrm dr},\\[4pt]\kappa_{\mathrm{abs}}&\simeq\frac{3k\,\mathrm{Im}(q)}{\rho},\qquad\kappa_{\mathrm{sca}}\simeq\frac{2k^4r^3|q|^2}{\rho}\end{aligned}
Notation legend
κ_ext, κ_abs, κ_sca: mass coefficients
Extinction, absorption, scattering (m²/kg)
C_ext(r): particle extinction cross section (m²)
p(r): particle number distribution in radius
r: physical particle radius (m)
ρ: particle material density (kg/m³)
k = 2π/λ: electromagnetic wavenumber (m⁻¹)
λ: wavelength in the surrounding medium (m)
q = (m² − 1)/(m² + 2): contrast factor
m: complex relative refractive index
Im(q): imaginary part of q
|q|²: squared complex magnitude
dr: radius integration element (m)
≃: Rayleigh approximation for small particles
The two final terms describe one radius r
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 13
Task 1.4 · PM definitions and the negative result
Output | Mass represented | Current result
PM1 | Below 1 µm aerodynamic diameter | Exploratory extra split fails numerical separation
PM2.5 | Fine mass below 2.5 µm | No useful mass retrieval in the tested grid
Coarse PM | Disjoint 2.5–10 µm mass | Nearly collinear with the fine-mode signature
PM10 | Fine plus coarse mass | Includes their covariance, no valid 95% limit
The fine model truncates below 0.03 µm. PM10 includes PM2.5, so they are not disjoint particle populations.
Fine Rayleigh/Mie difference
0.00086% RMS
Coarse difference
0.0201% RMS
Three-bin inverse identity error
0.508, rejected
A gain slope removes much of smooth Rayleigh absorption. Shared scattering shapes leave extremely weak size information.
Notation and units
PM₁₀: total fine plus coarse mass (µg/m³)
c_fine: modeled PM2.5 mass (µg/m³)
c_coarse: modeled 2.5–10 µm mass (µg/m³)
Var: variance of a concentration estimate
Cov: covariance between the two estimates
All variance terms have units (µg/m³)²
Fine and coarse bins are disjoint
PM₁₀ = c_fine + c_coarse
Their covariance must enter the total error
13
Notes: Fine assumptions: density 1500 kg/m³, median physical size 0.5 µm, geometric spread 1.7, refractive index 1.5 + 0.01i. Coarse: 1800 kg/m³, 4 µm, 1.6, 1.53 + 0.01i. Rayleigh/Mie RMS differences are 0.00086% fine and 0.0201% coarse in the earlier physical check. Three-bin scaled inverse identity error is approximately 0.508 and fails the gate.
LaTeX equation source
\mathrm{Var}(\mathrm{PM}_{10})=\mathrm{Var}(c_{\mathrm{fine}})+\mathrm{Var}(c_{\mathrm{coarse}})+2\,\mathrm{Cov}(c_{\mathrm{fine}},c_{\mathrm{coarse}})
Notation legend
PM₁₀: total fine plus coarse mass (µg/m³)
c_fine: modeled PM2.5 mass (µg/m³)
c_coarse: modeled 2.5–10 µm mass (µg/m³)
Var: variance of a concentration estimate
Cov: covariance between the two estimates
All variance terms have units (µg/m³)²
Fine and coarse bins are disjoint
PM₁₀ = c_fine + c_coarse
Their covariance must enter the total error
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/48_expanded_voc_pm_and_20s_calibration.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 14
Task 2.1 · Link budget and sequential receiver
Parameter / check | Value
Power / noise figure | 23 dBm / 6 dB
Implementation loss | 5 dB
Instantaneous bandwidth | 16 MHz
Settling per hop | 1 ms
Specified a 550 km downlink, 23 dBm active transmit power, 0.50 / 0.30 m apertures and a nominal 6 dB noise figure.
Replaced the ideal simultaneous broad reference with one RF chain hopping across sixteen 16 MHz blocks within 220–330 GHz.
R is range, F the linear noise factor and Limpl the linear implementation loss. Receiver noise figure enters once.
Each block has sixteen 1 MHz tones. CP, pilots, full frames, reference time and retuning all consume the time budget.
23 dBm across the selected bands and 6 dB receiver noise are unverified RF requirements.
Data and models used
ITU P.676: background and sky emission.
Task 1: HITRAN / IGRA propagation.
550 km, 23 dBm, 6 dB NF: scenarios.
Used to compute SNR and time budgets.
No measured RF chain dataset is used.
Power, noise and settling are requirements.
Notation and units
ν: frequency (Hz), λ: wavelength (m)
P_t, P_r: transmit and received power (W)
G_t, G_r: antenna power gains (linear)
L_impl: implementation loss (linear)
R: propagation distance (m)
A(ν): atmospheric attenuation (dB)
SNR: signal to noise power ratio (linear)
k: Boltzmann constant (J/K)
B: receiver noise bandwidth (Hz)
T_sky: sky noise temperature (K)
T₀: receiver noise reference temperature (K)
F: receiver noise factor (linear)
F = 10^(noise figure in dB / 10)
T₀(F − 1): receiver noise temperature (K)
Gains and losses must be converted from dB
14
Notes: Data and models used
ITU P.676: background and sky emission.
Task 1: HITRAN / IGRA propagation.
550 km, 23 dBm, 6 dB NF: scenarios.
Used to compute SNR and time budgets.
No measured RF chain dataset is used.
Power, noise and settling are requirements.
LaTeX equation source
\begin{aligned}P_r(\nu)&=\frac{P_t(\nu)G_t(\nu)G_r(\nu)}{L_{\mathrm{impl}}}\left(\frac{\lambda}{4\pi R}\right)^2 10^{-A(\nu)/10},\\[4pt]\mathrm{SNR}(\nu)&=\frac{P_r(\nu)}{kB\left[T_{\mathrm{sky}}(\nu)+T_0(F-1)\right]}\end{aligned}
Notation legend
ν: frequency (Hz), λ: wavelength (m)
P_t, P_r: transmit and received power (W)
G_t, G_r: antenna power gains (linear)
L_impl: implementation loss (linear)
R: propagation distance (m)
A(ν): atmospheric attenuation (dB)
SNR: signal to noise power ratio (linear)
k: Boltzmann constant (J/K)
B: receiver noise bandwidth (Hz)
T_sky: sky noise temperature (K)
T₀: receiver noise reference temperature (K)
F: receiver noise factor (linear)
F = 10^(noise figure in dB / 10)
T₀(F − 1): receiver noise temperature (K)
Gains and losses must be converted from dB
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/47_receiver_design_and_calibration.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 15
Task 2.1 · Resources and communication cost
Quantity | Current result
Total reference + sample time | 20 s, split equally
Actual frame transmission / retuning | 19.72 s / 0.032 s
Instantaneous bandwidth / RF chains | 16 MHz / one
Selected schedule Gaussian rate | 109.52 Mbit/s
Best tested fixed block Gaussian rate | 128.31 Mbit/s
Rate loss against that fixed block | 14.64%
The comparison uses equal instantaneous bandwidth, power and CP/pilot overhead. Both reference and sample carry payload.
Selected center range
224–318.67 GHz
Pilot / frame symbols
30 / 10,000
CP / useful symbol
1 / 16
Zero architecture cost is not established. Gaussian rate is different from coded QPSK throughput.
Notation and units
R̄: average Gaussian information rate (bit/s)
b: selected frequency block index
k: tone index within block b
t_b: transmission time in block b (s)
t_total: total acquisition time (s)
t_b / t_total: block’s time fraction
Δf: bandwidth per tone (Hz)
SNR_k: tone signal to noise ratio (linear)
log₂: base two logarithm
15
Notes: Best fixed block among tested candidates is centered at 224 GHz. This is not a global optimum over every possible communications design. The older 1.382% number isolates schedule counts and must not replace the full 14.64% comparison.
LaTeX equation source
\overline R=\sum_b\frac{t_b}{t_{\mathrm{total}}}\sum_{k\in b}\Delta f\log_2\!\left(1+\mathrm{SNR}_k\right)
Notation legend
R̄: average Gaussian information rate (bit/s)
b: selected frequency block index
k: tone index within block b
t_b: transmission time in block b (s)
t_total: total acquisition time (s)
t_b / t_total: block’s time fraction
Δf: bandwidth per tone (Hz)
SNR_k: tone signal to noise ratio (linear)
log₂: base two logarithm
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/communication_tradeoff.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 16
Task 2.2 · CSI and raw waveform simulation
Parameter / check | Value
Blocks / tones per block | 16 / 16
Frame length | 10,000 symbols
Pilots per frame | 30
Acquisition CFO stress | 100 kHz
Generated complex line-of-sight observations with frequency-dependent attenuation and additive complex Gaussian noise.
Added raw IFFT/CP frames, timing acquisition, Doppler correction, pilot tracking and coded packet checks.
Separate raw frames test modem behavior. Large recall experiments draw joint sample moments and apply nonlinear inversion.
The simulation connects physical channel attenuation to a bounded moving receiver.
The large recall study does not generate every raw waveform sample for every Monte Carlo trial.
Data and models used
Physics: Task 1. Receiver: Task 2.1.
Generated QPSK/OFDM observations.
16 raw frames: one per chosen block.
Used for timing and decoded-bit checks.
Recall trials use simulated moments.
No downloaded or measured CSI set.
Notation and units
k: tone index, n: time sample index
x_k: transmitted tone symbol
y_k: received tone symbol
h_k: complex channel coefficient
w_k: additive complex receiver noise
V_k: noise variance in symbol power units
CN(0,V_k): circular complex Gaussian noise
Its real / imaginary variances are V_k / 2
X_k: frequency domain OFDM symbols
x[n]: transmitted time domain samples
IFFT: inverse fast Fourier transform
h_k scales amplitude and rotates phase
16
Notes: Data and models used
Physics: Task 1. Receiver: Task 2.1.
Generated QPSK/OFDM observations.
16 raw frames: one per chosen block.
Used for timing and decoded-bit checks.
Recall trials use simulated moments.
No downloaded or measured CSI set.
LaTeX equation source
\begin{aligned}y_k&=h_kx_k+w_k,\qquad w_k\sim\mathcal{CN}(0,V_k),\\[4pt]x[n]&=\operatorname{IFFT}\{X_k\}\end{aligned}
Notation legend
k: tone index, n: time sample index
x_k: transmitted tone symbol
y_k: received tone symbol
h_k: complex channel coefficient
w_k: additive complex receiver noise
V_k: noise variance in symbol power units
CN(0,V_k): circular complex Gaussian noise
Its real / imaginary variances are V_k / 2
X_k: frequency domain OFDM symbols
x[n]: transmitted time domain samples
IFFT: inverse fast Fourier transform
h_k scales amplitude and rotates phase
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/scope_boundaries.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 17
Task 2.2 · What the waveform controls establish
Control | Retained result | Boundary
Selected-frequency coverage | 16 fresh raw frames | One frequency spot check per selected block
Timing acquisition | 16 / 16 correct | Bounded integer timing model
Passive sensing | Identical decoded outputs in every case | Comparison uses the same scheduled modem
Coded information errors | 1,391 errors | Across 2,826,240 information bits
Full mission dynamics | Still open | Fractional timing, clock drift and time dilation
Narrowband Doppler correction addresses carrier shift. Wideband time scaling requires additional receiver modeling.
Information bits
2,826,240
Information bit errors
1,391
Raw coded bit error rate
0.0492%
Oscillator noise, pointing, multipath and realistic reference availability remain open.
Notation and units
f_D: Doppler frequency shift (Hz)
f_c: carrier frequency (Hz)
v_r: signed radial relative velocity (m/s)
c: speed of light (m/s)
≃: first order narrowband approximation
The shift sign follows the velocity convention
17
Notes: These spot checks support bounded communication behavior, not a measured field recall or a continuous complete orbital pass. Selected_raw_frames.csv retains packet counts and residual CFO.
LaTeX equation source
f_D\simeq\frac{v_r}{c}\,f_c
Notation legend
f_D: Doppler frequency shift (Hz)
f_c: carrier frequency (Hz)
v_r: signed radial relative velocity (m/s)
c: speed of light (m/s)
≃: first order narrowband approximation
The shift sign follows the velocity convention
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/selected_raw_frames.csv
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/scope_boundaries.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 18
Task 3.1 · Joint spectral isolation
Parameter / check | Value
Unknown target masses | 7
Reported outputs | 8 with PM10
Selected frequencies | 256 tones
Scaled identity tolerance | 10⁻⁵
Fitted all five gas signatures and two PM modes simultaneously.
Whitened the observation covariance and projected out gain offset/slope, atmospheric background and four interfering gases.
D contains target signatures. N contains nuisance signatures. QN spans the whitened nuisance space. An SVD constructs H.
Numerical gates check scaled H D ≈ I and nuisance rejection H N ≈ 0.
No algorithm can separate an arbitrary gain error that occupies the same spectral direction as the pollutant.
Data and models used
Five target + four interfering gases.
HITRAN signatures and two PM modes.
Standard atmosphere selects 16 bands.
January IGRA checks weather transfer.
Used to build the joint inverse model.
No measured training labels are used.
Notation and units
a: attenuation vector (dB), e: error (dB)
D: target response matrix
c, ĉ: true / estimated concentrations (µg/m³)
N β: nuisance attenuation contribution (dB)
C = Cov(e): observation covariance (dB²)
N: nuisance response matrix
β: nuisance coefficients
Q_N: orthonormal whitened nuisance basis
P: projector away from nuisance space
I: identity matrix, T: matrix transpose
H: linear concentration retrieval operator
Bold symbols denote vectors or matrices
18
Notes: Data and models used
Five target + four interfering gases.
HITRAN signatures and two PM modes.
Standard atmosphere selects 16 bands.
January IGRA checks weather transfer.
Used to build the joint inverse model.
No measured training labels are used.
LaTeX equation source
\begin{aligned}\mathbf a&=\mathbf D\mathbf c+\mathbf N\boldsymbol\beta+\mathbf e,\qquad\mathbf C=\operatorname{Cov}(\mathbf e),\\[4pt]\mathbf P&=\mathbf I-\mathbf Q_N\mathbf Q_N^{\mathsf T},\qquad\widehat{\mathbf c}=\mathbf H\mathbf a\end{aligned}
Notation legend
a: attenuation vector (dB), e: error (dB)
D: target response matrix
c, ĉ: true / estimated concentrations (µg/m³)
N β: nuisance attenuation contribution (dB)
C = Cov(e): observation covariance (dB²)
N: nuisance response matrix
β: nuisance coefficients
Q_N: orthonormal whitened nuisance basis
P: projector away from nuisance space
I: identity matrix, T: matrix transpose
H: linear concentration retrieval operator
Bold symbols denote vectors or matrices
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/scripts/joint_receiver_support.py
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 19
Task 3.1 · Frequency selection improves five-gas inference
A deterministic coordinate-exchange screen selected sixteen blocks using the standard 45° design case.
The selection optimized the worst relative gas uncertainty while retaining PM and nuisance parameters. Exact tone spectra followed the coarse screen.
CH₃CN at 1 µg/m³ | Uniform bands | Selected bands
Simulated recall | 57.40% | 97.67%
Total acquisition time | 20 s | 20 s
Assumed residual standard deviation | 0.0001 dB | 0.0001 dB
Deterministic starts
3
Selected blocks
16
Improved exact gas limits
5 / 5
All five exact VOC information limits improve relative to the uniform design.
January weather and response draws did not choose bands. Global optimality and unknown-weather robustness remain unproved.
19
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. The fresh uniform control is 57.40%. The historical 56.63% value belongs to an earlier independent simulation. The selected result is a conditional improvement at equal resources.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/selection.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 20
Task 3.2 · Payload moments estimate signal and noise
Parameter / check | Value
Pilot fraction per frame | 0.3%
Payload fraction per frame | 99.7%
Signal moments | Second and fourth
Modulation tested | QPSK
Used the existing constant-modulus QPSK payload instead of discarding most samples and retaining only 30 pilots per 10,000 symbols.
Applied the established M2M4 estimator with a finite-sample correction, then compared sample and reference powers.
S is received signal power. V is noise power. The moments separate signal and noise under the QPSK and Gaussian-noise model.
More existing symbols contribute information without adding sensing transmissions.
Arbitrary QAM, nonlinear distortion or severe intercarrier interference invalidate these simple moments.
Data and models used
Generated QPSK moments, not field CSI.
10,000 trials per null/positive class.
Five VOC scenarios + PM mass controls.
HITRAN/IGRA define the forward model.
Used to estimate recall and mass error.
Earlier three-gas controls stay separate.
Notation and units
M₂: second moment E[|y|²]
M₄: fourth moment E[|y|⁴]
y: received complex symbol
E: expectation, |y|: complex magnitude
S: received signal power
V: receiver noise power
M₂, S, V share power units
M₄ has squared power units
A: differential attenuation (dB)
S_sample: signal power in sample observation
S_reference: signal power in reference
log₁₀: base ten logarithm
20
Notes: M2M4 is established prior work. The contribution is its application, resource accounting and conditional evaluation here. Invalid inversions count as failures. Large experiments use the joint asymptotic distribution of second/fourth sample moments and nonlinear inversion. Raw QPSK controls independently test bounded cases.
Data and models used
Generated QPSK moments, not field CSI.
10,000 trials per null/positive class.
Five VOC scenarios + PM mass controls.
HITRAN/IGRA define the forward model.
Used to estimate recall and mass error.
Earlier three-gas controls stay separate.
LaTeX equation source
\begin{aligned}M_2&=S+V,\qquad M_4=S^2+4SV+2V^2,\\[4pt]S&=\sqrt{2M_2^2-M_4},\qquad A=-10\log_{10}\!\left(\frac{S_{\mathrm{sample}}}{S_{\mathrm{reference}}}\right)\end{aligned}
Notation legend
M₂: second moment E[|y|²]
M₄: fourth moment E[|y|⁴]
y: received complex symbol
E: expectation, |y|: complex magnitude
S: received signal power
V: receiver noise power
M₂, S, V share power units
M₄ has squared power units
A: differential attenuation (dB)
S_sample: signal power in sample observation
S_reference: signal power in reference
log₁₀: base ten logarithm
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/42_payload_recall.md
https://arxiv.org/abs/2506.15998
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 21
Task 3.2 · Why payload reuse mattered
Earlier ideal broad reference, three target gases and zero persistent calibration residual
Historical control | Pilots | Payload M2M4 | Reference assumption
CH₃CN, 1 µg/m³, 10 s | 0.460% recall | 99.955% recall | Exactly known reference
CH₃CN, 1 µg/m³, 20 s total | 0.380% recall | 93.800% recall | 10 s independent reference + 10 s sample
Pilot samples per frame
30
Total symbols per frame
10,000
Old physical architecture
Ideal simultaneous broad bands
Payload moments recover information that sparse pilot-only sensing discards.
The ideal broad architecture and zero residual assumption prevent direct transfer to deployed hardware.
21
Notes: Historical results in docs/42_payload_recall.md. This table compares methods within each original control. It is separate from the current five-gas hopping receiver and its eight-output false-alarm family. M2M4 itself is established prior work.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/42_payload_recall.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/46_critical_calibration_assumption.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 22
Task 3.2 · Detection gains are species dependent
20 s total, assumed 0.0001 dB residual, selected bands and standard atmosphere at 45°
Gas | Recall at 1 (%) | Misses at 1 (%) | c95 µg/m³ | Recall at c95 (%) | 95% CI at c95 (%) | RMSE at c95 (%)
Formaldehyde | 0.77 | 99.23 | 7.846 | 95.12 | 94.68–95.53 | 21.14
Methanol | 0.75 | 99.25 | 8.838 | 95.12 | 94.68–95.53 | 21.24
Acetonitrile | 97.67 | 2.33 | 0.927 | 95.12 | 94.68–95.53 | 21.49
Chloromethane | 3.58 | 96.42 | 3.918 | 94.72 | 94.26–95.15 | 21.64
Formic acid | 0.16 | 99.84 | 30.550 | 94.85 | 94.40–95.28 | 21.55
Positive / null trials
10,000 / 10,000
Family false alarms
0.79%
Relative RMSE at 95% points
Approximately 21%
Acetonitrile reaches 97.67% recall at 1 µg/m³. Other gases require higher concentrations.
These are simulated detection frequencies, not measured field performance or concentration accuracy.
22
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. Each positive and null class has 10,000 trials. Exact CH3CN interval 97.355–97.957%. Family false alarms 0.79%. At nominal 95% detection points relative concentration RMSE is about 21%, not 5%.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/response_metrics.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 23
Task 4.1 · Lower bounds with nuisance parameters
Parameter / check | Value
Likelihoods | QPSK and magnitude
Unknown noise | Included
Finite reference | Included
Historical efficiency | 95.89–97.61%
Derived full QPSK and magnitude likelihood information with unknown signal power, noise power and finite reference uncertainty.
Profiled nuisance parameters before comparing the attainable concentration covariance with the estimator variance.
c denotes target concentration and η all nuisance parameters. The Schur complement accounts for their uncertainty.
The bound identifies when replacing the estimator offers little remaining gain.
The bound is local and conditional on the likelihood, covariance and physical signatures.
Data and models used
Analytical QPSK / magnitude likelihood.
Unknown signal, noise and reference.
Historical three-gas physical model.
Used for Fisher bounds and efficiency.
No independent measured dataset.
20 s, zero extra residual: benchmark.
Notation and units
y: observed signal data
θ: complete unknown parameter vector
p(y;θ): likelihood of the observations
E: expectation under the assumed model
J_ab: Fisher information entry for θ_a, θ_b
c: target concentration vector (µg/m³)
η: nuisance parameter vector
J_cc, J_cη, J_ηη: Fisher matrix blocks
J_eff: information after nuisance profiling
ĉ: estimated concentration vector
Cov(ĉ): estimator covariance, units (µg/m³)²
−1: matrix inverse, ⪰: covariance lower bound
23
Notes: Data and models used
Analytical QPSK / magnitude likelihood.
Unknown signal, noise and reference.
Historical three-gas physical model.
Used for Fisher bounds and efficiency.
No independent measured dataset.
20 s, zero extra residual: benchmark.
LaTeX equation source
\begin{aligned}J_{ab}&=\mathbb E\!\left[\frac{\partial\log p(y;\boldsymbol\theta)}{\partial\theta_a}\frac{\partial\log p(y;\boldsymbol\theta)}{\partial\theta_b}\right],\\[4pt]\mathbf J_{\mathrm{eff}}&=\mathbf J_{cc}-\mathbf J_{c\eta}\mathbf J_{\eta\eta}^{-1}\mathbf J_{\eta c},\qquad\operatorname{Cov}(\widehat{\mathbf c})\succeq\mathbf J_{\mathrm{eff}}^{-1}\end{aligned}
Notation legend
y: observed signal data
θ: complete unknown parameter vector
p(y;θ): likelihood of the observations
E: expectation under the assumed model
J_ab: Fisher information entry for θ_a, θ_b
c: target concentration vector (µg/m³)
η: nuisance parameter vector
J_cc, J_cη, J_ηη: Fisher matrix blocks
J_eff: information after nuisance profiling
ĉ: estimated concentration vector
Cov(ĉ): estimator covariance, units (µg/m³)²
−1: matrix inverse, ⪰: covariance lower bound
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/44_payload_information_derivation.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/45_payload_bounds_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 24
Task 4.1 · M2M4 is already close to the bound
Historical broad reference, three target gases, 20 s total and zero extra calibration residual
Gas | CRLB / M2M4 variance | Historical 95% limit µg/m³
Formaldehyde | 95.89% | 4.456
Methanol | 97.61% | 10.307
Acetonitrile | 96.49% | 1.023
Values near 100% leave little improvement available from estimator replacement in this control.
Historical output family
6
Acquisition split
10 s + 10 s
Calibration benchmark
Zero extra residual
The next substantial improvement came from frequency information and design.
These historical bounds use a different architecture and target family from the current five-gas receiver.
Notation and units
Efficiency: lower bound / estimator variance
Displayed percentage = 100 × this ratio
Variance lower bound: conditional CRLB
CRLB: Cramér–Rao lower bound
Estimator variance: variance of M2M4 output
Both variances use the same concentration units²
24
Notes: Standard atmosphere at 45°, charged 10 s reference plus 10 s sample, unknown noise and joint spectral nuisance. The prior six-output family differs from the current eight-output family. Do not use this table to rank current and old designs as equal conditions.
LaTeX equation source
\mathrm{Efficiency}=\frac{\text{variance lower bound}}{\text{estimator variance}}
Notation legend
Efficiency: lower bound / estimator variance
Displayed percentage = 100 × this ratio
Variance lower bound: conditional CRLB
CRLB: Cramér–Rao lower bound
Estimator variance: variance of M2M4 output
Both variances use the same concentration units²
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/45_payload_bounds_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 25
Task 4.2 · Time and calibration jointly set uncertainty
Parameter / check | Value
Time grid | 2 / 20 / 100 s
Residual grid | 0 / 0.0001 / 0.001 dB
Noise-figure grid | 6 / 17 dB
Calibration draws | Once per acquisition
Recomputed the link, absorption, emission and target fit when weather, elevation, bands or receiver noise change.
The latest common grid contains every VOC, PM2.5, coarse PM and PM10 in every operating condition.
Thermal variance decreases with retained symbols. The additional calibration residual persists through the acquisition.
More time helps until persistent calibration error dominates.
The 10 GHz correlation length and each calibration standard deviation remain unmeasured assumptions.
Data and models used
HITRAN gas signatures and PM model.
ITU standard + January IGRA profile.
288 settings; 8 outputs; 2,304 rows.
Time 2/20/100 s, residual 0–0.001 dB.
Used for the common sensitivity grid.
These are generated model outputs.
Notation and units
C: attenuation covariance matrix (dB²)
t: total reference plus sample time (s)
t / 2: time assigned to each observation
V_sample, V_reference: variance vectors (dB²)
diag: diagonal matrix built from a vector
σ_cal: persistent residual standard deviation (dB)
K: dimensionless spectral correlation matrix
K_ij: correlation of frequency bins i and j
ν_i, ν_j: bin frequencies in matching units
10 GHz: assumed spectral correlation length
exp: exponential function
σ_cal² K: persistent covariance contribution
25
Notes: Data and models used
HITRAN gas signatures and PM model.
ITU standard + January IGRA profile.
288 settings; 8 outputs; 2,304 rows.
Time 2/20/100 s, residual 0–0.001 dB.
Used for the common sensitivity grid.
These are generated model outputs.
LaTeX equation source
\begin{aligned}\mathbf C(t,\sigma_{\mathrm{cal}})&=\operatorname{diag}\!\left[\mathbf V_{\mathrm{sample}}(t/2)+\mathbf V_{\mathrm{reference}}(t/2)\right]+\sigma_{\mathrm{cal}}^2\mathbf K,\\[4pt]K_{ij}&=\exp\!\left(-\frac{|\nu_i-\nu_j|}{10\,\mathrm{GHz}}\right)\end{aligned}
Notation legend
C: attenuation covariance matrix (dB²)
t: total reference plus sample time (s)
t / 2: time assigned to each observation
V_sample, V_reference: variance vectors (dB²)
diag: diagonal matrix built from a vector
σ_cal: persistent residual standard deviation (dB)
K: dimensionless spectral correlation matrix
K_ij: correlation of frequency bins i and j
ν_i, ν_j: bin frequencies in matching units
10 GHz: assumed spectral correlation length
exp: exponential function
σ_cal² K: persistent covariance contribution
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/global_comparison_protocol.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 26
Task 4.2 · Longer time cannot remove calibration error
Acetonitrile at 1 µg/m³, selected bands, standard atmosphere at 45°
Chart: Simulated recall (%)
| 2 s | 20 s | 100 s
0 dB | 7.58 | 99.28 | 100
0.0001 dB | 7.6 | 97.67 | 100
0.001 dB | 2.24 | 4.36 | 5.05
Parameter / check | Value
20 s, 0 dB | 99.28% recall
20 s, 0.0001 dB | 97.67% recall
20 s, 0.001 dB | 4.36% recall
100 s, 0.001 dB | 5.05% recall
At 0.001 dB, recall is only 4.36% at 20 s and 5.05% at 100 s.
Zero and nonzero residuals are sensitivity assumptions. No receiver stability measurement establishes them.
26
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. Curves use separate finite Monte Carlo samples. The 100% observed values retain confidence intervals below perfect population recall. The covariance is persistent within each acquisition.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/response_metrics.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 27
Task 4.2 · PM shares the full global comparison
Variable | Compared settings
Frequency plan | Uniform and selected sixteen-block schedules
Atmosphere | Standard and January sounding
Elevation | 30°, 45°, 60°, 90°
Reference + sample time | 2 s, 20 s, 100 s
Assumed calibration residual | 0, 0.0001, 0.001 dB
Receiver noise figure | 6 dB and 17 dB
Common result rows
2,304
Rejected settings
Standard, 30°, NF 17 dB
PM predicted recall
Approximately 0.125%
288 conditions × 8 outputs = 2,304 rows. Each output has 270 computed and 18 rejected conditions.
No valid 95% response limit for PM2.5 or PM10 anywhere in this grid.
27
Notes: Fixed 23 dBm transmit power, matched reference weather, 10 GHz residual correlation. All rejected cases are standard atmosphere, 30° elevation, 17 dB noise figure for both schedules and all times/calibrations. Their target separation fails the numerical gate. Failed rows remain present and do not receive fabricated zero recall.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/global_comparison.csv
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/global_comparison_protocol.json
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 28
Task 4.3 · Detection limits and percentage definitions
Parameter / check | Value
One-sided target α | 0.01 / 8 = 0.00125
Null threshold z | Approximately 3.023
Positive power target | 95%
Absorption cap | 1 dB
Fixed a 1% family false-alarm budget across eight outputs before observing outcomes.
Solved the concentration for nominal 95% power using positive-signal variance, then tested it with fresh simulated responses.
Positive absorption changes SNR and variance. The solution stays within at most 1 dB added absorption.
Reports include low recalls, missed detections, exact binomial intervals and concentration RMSE.
95% detection power, a 95% confidence interval and 5% concentration error describe different quantities.
Data and models used
Current positive/null response trials.
480 retained percentage/error rows.
Used for limits, recall and intervals.
WHO 2021 PM levels: comparison only.
15/45 µg/m³: declared PM controls.
No field compliance dataset is available.
Notation and units
Φ⁻¹: inverse standard normal CDF
z: dimensionless null detection threshold
0.01: family false alarm probability budget
8: number of reported outputs
ĉ_j: estimate for target j (µg/m³)
s_null: standard deviation under the null
s_positive(c): standard deviation at mass c
Both standard deviations use µg/m³
c₉₅: concentration for 95% recall (µg/m³)
1.64485: Φ⁻¹(0.95), a normal quantile
>: target detection decision
The variance depends on positive concentration
28
Notes: Recall = TP/(TP+FN). False alarms = FP/(FP+TN). Relative RMSE = sqrt(mean((estimate−truth)^2))/truth. Precision and F1 use artificial 50% prevalence. A missing in-domain solution remains unavailable. The PM10 output participates in the family although it derives from two masses.
Data and models used
Current positive/null response trials.
480 retained percentage/error rows.
Used for limits, recall and intervals.
WHO 2021 PM levels: comparison only.
15/45 µg/m³: declared PM controls.
No field compliance dataset is available.
LaTeX equation source
\begin{aligned}z&=\Phi^{-1}\!\left(1-\frac{0.01}{8}\right),\qquad\widehat c_j>z\,s_{\mathrm{null}},\\[4pt]c_{95}&=z\,s_{\mathrm{null}}+1.64485\,s_{\mathrm{positive}}(c_{95})\end{aligned}
Notation legend
Φ⁻¹: inverse standard normal CDF
z: dimensionless null detection threshold
0.01: family false alarm probability budget
8: number of reported outputs
ĉ_j: estimate for target j (µg/m³)
s_null: standard deviation under the null
s_positive(c): standard deviation at mass c
Both standard deviations use µg/m³
c₉₅: concentration for 95% recall (µg/m³)
1.64485: Φ⁻¹(0.95), a normal quantile
>: target detection decision
The variance depends on positive concentration
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/scripts/evaluate_joint_receiver.py
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 29
Task 4.3 · Every 95% limit needs time and calibration
Nominal 95% response concentration in µg/m³, selected bands, standard atmosphere at 45°
Total s | Residual dB | H₂CO | CH₃OH | CH₃CN | CH₃Cl | HCOOH
2 | 0 | 25.778 | 27.695 | 2.917 | 12.206 | 102.781
2 | 0.0001 | 25.862 | 27.911 | 2.938 | 12.309 | 102.894
2 | 0.001 | 33.018 | 44.262 | 4.550 | 19.693 | 113.332
20 | 0 | 7.568 | 8.131 | 0.856 | 3.584 | 30.171
20 | 0.0001 | 7.846 | 8.838 | 0.927 | 3.918 | 30.550
20 | 0.001 | 21.913 | 35.377 | 3.557 | 15.567 | 56.267
100 | 0 | 3.361 | 3.612 | 0.380 | 1.592 | 13.400
100 | 0.0001 | 3.945 | 4.999 | 0.517 | 2.226 | 14.228
100 | 0.001 | 20.826 | 34.603 | 3.468 | 15.192 | 49.310
CH₃CN, 20 s / 0.0001 dB
0.927 µg/m³
CH₃CN, 100 s / 0.001 dB
3.468 µg/m³
Valid PM limits in nine cases
0
PM2.5, coarse PM and PM10 have no valid 95% response limit in these nine conditions.
29
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. Values solve positive-response variance and precede Monte Carlo evaluation. Actual simulated recalls near 95% remain as measured fractions in the response CSV. All calibration levels are assumed.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/response_metrics.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 30
Task 4.3 · Environmental interpretation remains open
Parameter / check | Value
H₂CO current limit ppm | 0.006179
CH₃CN current limit ppm | 0.000534
Limit conditions | 20 s / 0.0001 dB
Ambient PM test masses | 15 and 45 µg/m³
Converted gas mass to surface-equivalent mole fraction using pressure, temperature and molar mass.
Observable: short slant-path enhancement relative to a reference. Ambient guidance has distinct location and averaging requirements.
PM reference masses are 15 and 45 µg/m³. These tests do not establish compliance.
The numeric conversion assumes the displayed mass and molar-mass units. PM has mass units and no gas ppm conversion.
The study reports conditional floors and an explicit negative / unverified standards assessment.
Unknown baseline abundance, vertical profiles, PM information and independent truth prevent a positive compliance claim.
Notation and units
χ_ppm: gas mole fraction in ppm
c: gas mass concentration in µg/m³
M: gas molar mass in g/mol
R: ideal gas constant, 8.314 J/(mol K)
T: local absolute temperature (K)
p: local atmospheric pressure (Pa)
1 ppm = 10⁻⁶ mol/mol
The stated mass units cancel the 10⁶ factor
This gas conversion does not apply to PM
30
Notes: The prior standards review discusses WHO 2021 ambient PM guidelines and separate indoor formaldehyde guidance. These are different domains and time averages. This presentation does not interpret short radio enhancements as regulatory measurements.
LaTeX equation source
\chi_{\mathrm{ppm}}=\frac{c_{\mu\mathrm{g}/\mathrm m^3}\,R\,T}{p\,M_{\mathrm g/\mathrm{mol}}}
Notation legend
χ_ppm: gas mole fraction in ppm
c: gas mass concentration in µg/m³
M: gas molar mass in g/mol
R: ideal gas constant, 8.314 J/(mol K)
T: local absolute temperature (K)
p: local atmospheric pressure (Pa)
1 ppm = 10⁻⁶ mol/mol
The stated mass units cancel the 10⁶ factor
This gas conversion does not apply to PM
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/45_payload_bounds_results.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/41_measurement_protocol.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 31
Calibration is the critical engineering requirement
Parameter / check | Value
Required local σ at 20 s | About 0.000146 dB
Nominal random σ | 0.0001 dB
Power change for 0.0001 dB | About 0.002303%
Field calibration records | None
Zero calibration error means zero additional differential residual after modeled corrections. Thermal noise and reference uncertainty still remain.
At 20 s, the local CH₃CN requirement for 95% power at 1 µg/m³ is approximately 0.000146 dB residual standard deviation under the nominal covariance.
A persistent signed bias can move both the null threshold and the positive response in the adverse direction.
Calibration requirements are now quantitative and retained with every result.
A small random standard deviation does not guarantee resistance to arbitrary drift or unknown hop gains.
Notation and units
b_i: persistent bias in attenuation bin i (dB)
ε: upper bound on each |b_i| (dB)
i: spectral bin, j: retrieved target
H_j: row j of the concentration operator
‖H_j‖₁: sum of absolute row coefficients
B_j: resulting concentration bias bound (µg/m³)
s_j: concentration standard deviation (µg/m³)
z: null threshold, 1.64485: 95% normal quantile
c₉₅,protected: bias protected limit (µg/m³)
≃: local approximation with constant variance
31
Notes: The 0.000146 dB number is a local requirement, not a measured achieved accuracy. Independent hop-gain nuisance terms make the current separation unstable. Prior zero-calibration headline controls are retained separately in the permanent calibration note.
LaTeX equation source
\begin{aligned}|b_i|&\leq\varepsilon\quad\Longrightarrow\quad B_j=\varepsilon\,\lVert\mathbf H_j\rVert_1,\\[4pt]c_{95,\mathrm{protected}}&\simeq(z+1.64485)s_j+2B_j\end{aligned}
Notation legend
b_i: persistent bias in attenuation bin i (dB)
ε: upper bound on each |b_i| (dB)
i: spectral bin, j: retrieved target
H_j: row j of the concentration operator
‖H_j‖₁: sum of absolute row coefficients
B_j: resulting concentration bias bound (µg/m³)
s_j: concentration standard deviation (µg/m³)
z: null threshold, 1.64485: 95% normal quantile
c₉₅,protected: bias protected limit (µg/m³)
≃: local approximation with constant variance
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/46_critical_calibration_assumption.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/calibration_requirements.csv
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/50_species_methods_and_percentage_guide.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 32
Failures that constrain the claimed achievement
Failure or stress | Finding | Implication
PM mass and extra size split | Negligible useful information / unstable inverse | A successful optimizer cannot repair missing information
Unknown relative hop gains | Target separation fails | Requires calibrated relative spectral response
Weather mismatch | Frozen standard operator acquires bias | Matched-weather success is insufficient
Unamplified RF converter | Fails usable-SNR gate | Nominal power requires a complete RF chain
Modulation / receiver mismatch | Simple payload moments may become invalid | Receiver assumptions need dedicated validation
Numerically rejected global cases
18 / 288
Useful PM limits
0 / 270 valid cases
Gaussian architecture rate loss
14.64%
The intended general atmospheric VOC/PM instrument remains an open research outcome.
32
Notes: All listed failures remain in the current audit and retained stress outputs. The nominal 17 dB noise-figure grid also rejects standard atmosphere at 30° for both schedules. Successful runs do not conceal those cases.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/stress_sensitivity.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 33
Remaining problems and evidence needed
Open problem | Evidence required to close it
RF hardware and calibration | Measured power, noise, settling, spectral covariance and drift at selected tones
PM mass / composition | Paired optical properties, humidity, particle size and independent mass truth
Weather and concentration profiles | Independent profiles, column information and reference abundance
Full receiver dynamics | Continuous time-scaled channel with fractional timing, oscillator and pointing errors
Independent validation | Separate calibration and test campaigns with paired radio / concentration data
Deployment and environmental use | Applicable averaging domain, spectrum coordination and realistic operational coverage
Nominal RF target
23 dBm, NF 6 dB
Current calibration assumption
0.0001 dB
Current physical truth
No paired radio/VOC/PM test
33
Notes: Complete remaining-work ledger: docs/49_completion_audit_and_fixes.md. Additional unresolved details include unequal dwell/global frequency optimization, spectroscopy uncertainty, real-time hardware latency, atmospheric horizontal variability and communication coding/adaptation baselines.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/41_measurement_protocol.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 34
Proposed next experiments
Priority | Experiment | Decision it enables
1 | Repeated blank / reference acquisitions at selected tones | Can the required differential stability be achieved?
2 | Controlled gas path with independent concentration truth | Does the predicted VOC recall survive real model error?
3 | PM cell with known mass, size and humidity | Does radio information separate mass from composition?
4 | Full receiver and reference schedule under motion | Can the sensing result survive operational timing?
Calibration acceptance question
σ ≤ about 0.000146 dB at 20 s?
Frozen test target
1 µg/m³ CH₃CN
Independent test measurements
Still required
Freeze calibration and model choices before evaluating an independent test campaign.
Additional Monte Carlo trials improve numerical precision but cannot replace missing measurements.
34
Notes: These are proposed next experiments. No campaign has been completed or funded by this presentation. Before hardware access, full warped-time simulation and an additional PM observable are the most useful computational follow-ups.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/41_measurement_protocol.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 35
What we can report to the supervisor
Parameter / check | Value
Task implementations | 11 / 11
Verified research checks | 25,172
Conditional CH₃CN recall | 97.67%
Validated field recall | Unavailable
The original eleven modeling and simulation tasks now have implementations with traceable outputs.
Payload reuse and frequency selection improve conditional VOC detection. Acetonitrile reaches 97.67% recall at 1 µg/m³ with 20 s and assumed 0.0001 dB residual.
The analysis explains why PM remains weak and why more averaging cannot overcome persistent calibration error.
The next milestone is independent physical validation of the selected receiver and its concentration estimates.
The main achievement is a reproducible feasibility assessment and a stronger, explicitly conditional VOC design.
Useful joint PM retrieval, zero communication architecture cost and validated field performance remain unachieved.
35
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. The current schedule loses 14.64% Gaussian rate against the best tested fixed block. Source snapshot 461a3ba retains 235 tests and 25,172 numerical checks. These verify implementation and consistency, not physical truth.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 36
Appendix · Global VOC and PM outcomes
Envelopes over 270 valid operating conditions per output, with 18 additional rejected conditions
Output | Reference µg/m³ | Predicted recall range | Valid 95% limits / 270
H2CO | 1 | 0.128–89.043% | 270
CH3OH | 1 | 0.130–72.886% | 270
CH3CN | 1 | 0.282–100.000% | 270
CH3Cl | 1 | 0.139–100.000% | 270
HCOOH | 1 | 0.125–12.651% | 269
PM2.5 | 15 | 0.125–0.125% | 0
PMcoarse | 45 | 0.125–0.125% | 0
PM10 | 45 | 0.125–0.125% | 0
Grid
2 plans × 2 weather × 4 elevations
Other axes
3 times × 3 residuals × 2 noise figures
Mass assumptions
1 / 15 / 45 µg/m³ (see table)
Different reference concentrations and operating conditions prevent a direct same-condition species ranking.
36
Notes: These are conditional predictions using positive-response variance, not Monte Carlo frequencies. Ranges are operating-condition envelopes, not confidence intervals. Full 288-condition axes appear on Task 4.2 slides. Power fixed at 23 dBm and reference weather matched.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/global_comparison.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 37
Appendix · Low PM recalls remain visible
Simulated recall, selected bands, standard atmosphere at 45°, same joint five-gas fit
Total s | Residual dB | PM2.5 at 15 µg/m³ | Coarse at 45 µg/m³ | PM10 at 45 µg/m³
2 | 0 | 0.14% | 0.14% | 0.12%
2 | 0.0001 | 0.10% | 0.10% | 0.06%
2 | 0.001 | 0.09% | 0.11% | 0.14%
20 | 0 | 0.11% | 0.15% | 0.16%
20 | 0.0001 | 0.15% | 0.07% | 0.14%
20 | 0.001 | 0.15% | 0.19% | 0.09%
100 | 0 | 0.15% | 0.12% | 0.10%
100 | 0.0001 | 0.08% | 0.13% | 0.07%
100 | 0.001 | 0.07% | 0.10% | 0.13%
PM10 positive mixture
Fine 49/90, coarse 41/90
Null target threshold
0.125% theoretical marginal rate
Monte Carlo class size
10,000
These recalls are near the false-alarm scale. No cell establishes useful PM detection.
37
Notes: Selected bands, standard atmosphere, 45°, matched reference, 23 dBm and 6 dB noise figure. PM10 positive injection uses fine/coarse fractions 49/90 and 41/90. Each class has 10,000 trials. Binomial variation explains small nonmonotonic differences near the null rate. PM10 variance includes the cross covariance.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/joint_receiver_revision/response_metrics.csv
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 38
Appendix · Reproducible evidence map
Research snapshot 461a3ba, 27 September 2026
Research material | Repository location
Original task definition | I2R_proposal_THz_ISAC (1).pdf
Current results and global comparison | docs/51_joint_design_time_calibration_results.md
Species, equations and metric definitions | docs/50_species_methods_and_percentage_guide.md
Complete open-issue ledger | docs/49_completion_audit_and_fixes.md
Critical calibration record | docs/46_critical_calibration_assumption.md
Data, trials, hashes and validation | results/joint_receiver_revision/
Current manuscript | output/pdf/thz_isac_pollutant_sensing_ieee.pdf
Retained metric rows
480
Global rows
2,304
Passing research tests
235
38
Notes: Repository: https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring . The snapshot contains 235 passing tests and 25,172 numerical checks. These counts describe the computational research snapshot, not slide validation or independent physical evidence.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/49_completion_audit_and_fixes.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/51_joint_design_time_calibration_results.md
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 39
Appendix · Physical and methodological sources
Parameter / check | Value
Original tasks | 11
Current source snapshot | 461a3ba
Additional organic catalog gaps | 4
Paired field validation | Open
HITRAN2024 and HAPI: line data, isotope handling and spectroscopic calculations.
ITU-R P.835 and P.676: reference atmosphere, oxygen/water absorption and atmospheric background.
NOAA IGRA: independent measured weather soundings.
Aliaga et al. (2024) and Yang et al. (2024): satellite differential absorption and gas/particle propagation context.
Xu, Fu and Kim (2025): using pilots and payloads for sensing. Established M2M4 literature supplies the signal/noise estimator.
Published models motivate and parameterize the study. They do not validate this receiver’s field performance.
39
Notes: Sources:
HITRAN2024: https://hitran.org/media/refs/HITRAN-2024.pdf
HAPI: https://doi.org/10.1016/j.jqsrt.2016.03.005
ITU-R P.835-7: https://www.itu.int/rec/R-REC-P.835
ITU-R P.676-13: https://www.itu.int/rec/R-REC-P.676
NOAA IGRA: https://www.ncei.noaa.gov/products/weather-balloon/integrated-global-radiosonde-archive
Aliaga et al.: https://doi.org/10.1109/JSTARS.2024.3480816
Yang et al.: https://doi.org/10.1109/OJCOMS.2024.3386759
Xu et al.: https://arxiv.org/abs/2506.15998
M2M4: Gianmarco Romano, 2021, doi:10.3390/s21154950. See full references in current manuscript.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/paper/current_study.tex
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 40
Datasets · Exact HITRAN subset in the current receiver
HITRAN2024 via HAPI. The current nine gases use two retained input tables and isotope-specific profiles.
Gas and role | HITRAN isotope IDs | Acquired lines, 0–3000 GHz | Centres in 220–330 GHz
H2CO · target | 1, 2, 3 | 12,147 | 151
CH3OH · target | 1 | 4,663 | 467
CH3CN · target | 1 | 17,880 | 1,078
CH3Cl · target | 1, 2 | 12,824 | 670
HCOOH · target | 1, 2 | 18,440 | 401
CO · interferent | 1, 2, 3, 4, 5, 6 | 773 | 27
O3 · interferent | 1, 2, 3, 4, 5 | 93,018 | 3,199
SO2 · interferent | 1, 2, 3, 4 | 139,086 | 5,562
NO2 · interferent | 1 | 20,170 | 706
Acquired line pool
319,001
Isotope tables
25
Centres in receiver window
12,261
All acquired line wings enter the calculation. H₂O/O₂ background uses ITU-R P.676; these are parameters, not measured radio data.
40
Notes: Input file hashes were checked against the current physics manifest. The two pools contain 287,737 and 31,264 rows. The molecular cross section function uses no wing cutoff by default. Centre counts in 220–330 GHz are descriptive and do not define a filter. HITRAN supplies line positions, strengths, air broadening, lower state energy, temperature exponents and pressure shifts. HAPI provides isotope masses and TIPS partition sums. Earlier 34-table acquisition totals belong to a broader historical catalog.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/presentation_source_audit/dataset_subsets.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/payload_bounds/spectroscopy_acquisition.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/receiver_design/voc_pm_extension/acquisition.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/scripts/joint_receiver_support.py
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/src/thz_isac/physical_spectroscopy.py
https://hitran.org
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 41
Datasets · NOAA IGRA weather profiles actually used
Beijing station CHM00054511, 2026 year to date archive acquired on 23 September 2026.
Sounding, UTC | Measured levels | Measured top above station | Where it was used
2026-01-01 00:00 | 226 | 36.97 km | Current global grid and earlier tests
2026-04-01 00:00 | 160 | 28.76 km | Earlier seasonal sensitivity tests
2026-07-01 00:00 | 203 | 32.34 km | Earlier seasonal sensitivity tests
2026-09-01 00:00 | 189 | 34.95 km | Earlier seasonal sensitivity tests
Retained levels
103,322
Retained soundings
521
Selected profiles
4 earlier / 1 current
Current global comparisons use the January sounding and the ITU standard atmosphere.
Measured weather provides no VOC/PM concentration labels. Above the measured top, the atmosphere is extended by a model to 100 km.
41
Notes: The retained parser output contains 103,322 levels across 521 soundings. The declared selection was the first complete sounding reaching at least 20 km in January, April, July and September, before spectroscopy evaluation. Temperature, pressure and water profiles drive propagation. A model continues above the measured profile. The current receiver uses January as a weather check; band selection uses the standard atmosphere. The archive is a frozen year to date snapshot, not a complete year or global weather sample.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/task_completion/weather_selection.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/task_completion/source_acquisition.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/scripts/receiver_design_physics.py
https://www.ncei.noaa.gov/pub/data/igra/data/data-y2d/CHM00054511-data-beg2026.txt.zip
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 42
Datasets · Independent water and aerosol checks
These are external physical checks. Neither dataset supplies the current five VOC and PM recall labels.
Source | Exact part used | What was checked | Important boundary
Water vapour paper (2023) Scientific Reports, Figure 8 | Figure 8 aggregate slopes at 380.197353 GHz: VNA 0.033 ± 0.009 and TDS 0.027 ± 0.009 | Absorption slope in (dB/m)/(g/m³), compared with declared model states | Published aggregates only. No raw measurement series or VOC labels.
Calcite THz-TDS DOI 10.57745/DLJEFW, v1.0 | 8 sample and 4 blank recordings, 1 m path. Four native bins near 300, 325, 350 and 375 GHz. | Native FFT transmission with before/after blanks. 64 transmission rows. | No mass concentration or size labels. Cannot calibrate PM mass extinction.
Calcite observations
8 samples + 4 blanks
Native frequency resolution
About 25 GHz
Paired PM mass truth
Unavailable
Calcite reference RMS difference is 0.0472 dB. This is a separate laboratory diagnostic, not the current receiver’s calibration covariance.
42
Notes: Calcite particles were resuspended in dry nitrogen. All 12 recordings were analyzed with native FFT resolution around 25 GHz and no synthetic frequency refinement. Two blanks per reference phase were combined geometrically. Published calcite data have no concentration or size distribution labels. Water slopes are copied from the retained Figure 8 audit; their reported plus/minus values are not reinterpreted as confidence intervals. VNA comparison lies within the reported range, while the mean TDS comparison does not.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/five_task_closure/published_water_validation.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/five_task_closure/calcite_validation.json
https://doi.org/10.1038/s41598-023-47586-8
https://doi.org/10.57745/DLJEFW
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 43
Datasets · Earlier Beijing benchmark and its filters
Historical pollution inversion and ground sensor branches. These rows do not label the current five VOC recall experiments.
Stage | Exact retained subset or procedure
UCI Beijing Multi Site Air Quality | DOI 10.24432/C5RK5G. 12 sites, 1 March 2013 to 28 February 2017.
Raw measurements | 420,768 station hours. Six pollutants: CO, O₃, SO₂, NO₂, PM2.5 and PM10.
Complete case filter | 383,585 rows with required pollutants, temperature, pressure, dew point, rain and wind speed.
Particle consistency filter | Removed 17,642 rows where PM10 < PM2.5. Retained 365,943 physically ordered rows.
Modeling sample | Sort by timestamp and station. Select 20,000 deterministic evenly spaced rows.
Chronological evaluation | 12,000 train / 4,000 validation / 4,000 test. Normalize by the training Q95 − Q05 span.
Complete case retention
91.163%
Physically ordered rows
365,943
Scored modeling sample
20,000
Beijing concentrations are measured. The atmospheric THz spectra generated from them are simulated; later work reused the known test period.
43
Notes: This slide describes the principal physically filtered Beijing benchmark contract documented in the historical data provenance audit. The original cleaner excludes source wind direction. Complete case filtering may bias station and episode representation. Ground sensor forecasting and artificial channel masking are separate tasks from THz inversion. The current five VOC experiment uses controlled concentration scenarios, not these six pollutant rows.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/35_data_provenance_and_synthetic_evidence_audit.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/scripts/download_external_data.py
https://doi.org/10.24432/C5RK5G
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.

## Slide 44
Datasets · Other historical controls and unused sources
These sources support separate controls and historical studies, not a measured atmospheric VOC/PM receiver demonstration.
Source / branch | Part actually used | Role and evidence boundary
ESA CCI CO and NO₂ columns | March–December 2013, ten paired monthly rows. Grid centre 39.5° N, 116.5° E. | IASI/MOPITT CO total columns and OMI NO₂ tropospheric columns. Retrievals used for modeled feasibility.
Mendeley protein THz-TDS DOI 10.17632/dpw4svmdr8.1 | Fig3.csv: 7 lysozyme levels. Fig4.csv: 6 ovalbumin levels. Five bins from 0.9 to 1.3 THz. | Laboratory concentration control. Means and SDs only, with one concentration level held out at a time.
UCI Air Quality, Italy DOI 10.24432/C59K5F | 6,941 complete rows after removing −200 missing values. Split 4,164 / 1,388 / 1,389. | Four analyzer targets, five metal oxide sensors and weather. Earlier field calibration task, not THz.
NASA Aura MLS | Metadata resolved; no granules acquired or scored. | Investigated option only. It must not be counted as an evaluated measurement dataset.
ESA extract
10 months / 20 files
Protein files scored
2 of 10 downloaded
Current paired radio / truth set
None
The Italian branch has a weaker reproduction record. WHO and ITU documents supply benchmarks or models, rather than observation datasets.
44
Notes: ESA extraction used 20 files, two species across ten months, with quality and coordinate checks. Mendeley acquisition downloaded ten files but only Fig3.csv and Fig4.csv fed the reported concentration score; no pseudo replicates were generated. The Italian source contains 9,358 raw hourly rows from March 2004 to February 2005, in an unnamed city, but the detailed historical audit reports no dedicated committed downloader or scoring manifest for that branch. Source and branch limitations are preserved.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/docs/53_dataset_subsets_and_roles.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/docs/35_data_provenance_and_synthetic_evidence_audit.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/tables/real_column_feasibility_manifest.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/461a3ba/results/tables/measured_thz_control_manifest.json
https://doi.org/10.17632/dpw4svmdr8.1
https://doi.org/10.24432/C59K5F
Research snapshot 461a3ba. Predictions and simulations remain distinct from measured field performance.