## Slide 1
How a gas concentration
becomes a receiver decision
Acetonitrile at 90°: one complete numerical calculation
Actual HITRAN parameters, explicit arithmetic and a simulated receiver
5 October 2026
Notes: Assume a general telecommunications background. The question is how the project turns a concentration profile into a frequency dependent channel change, then estimates that concentration from noisy measurements. This is the same saved example as the earlier table, now with every physical and statistical step exposed. The spectroscopy records are real database inputs. The concentration profile, hardware and errors are model inputs; the receiver observations are simulated.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 2
What the four numbers in the original table mean
Number | Its role in the calculation
50.5814 µg/m³ | Chosen true enhancement q for this simulated experiment
0.012181 dB | Predicted extra attenuation of the first tone
0.998599 | Predicted sample/reference amplitude ratio for that tone
0.1401% | The same amplitude change expressed as a reduction
The last three values follow from q and the molecular absorption model. None is a receiver estimate.
q was chosen from the model’s 95% detection limit, before generating the observation. It is not a measured concentration.
Saved CH₃CN example · numerical steps and sources in notes
02
Notes: q is a controlled input; the other three quantities are deterministic predictions from that input. First derive 0.012181 dB from the actual spectroscopy and an assumed profile. Then derive the amplitude ratio. Finally add the modeled observation errors and calculate an estimate, which is 39.4247 µg/m³ for the saved draw. The reason for selecting 50.5814 is explained after deriving the detector.
Conditions
q was chosen from the model’s 95% detection limit, before generating the observation. It is not a measured concentration.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 3
q describes an enhancement with a fixed vertical shape
Altitude z | Sample minus reference concentration
0 m | 50.5814 µg/m³
500 m | 36.2432 µg/m³
1500 m | 18.6079 µg/m³
3000 m | 6.8454 µg/m³
5000 m | 1.8044 µg/m³
q is the unknown surface equivalent increase (µg/m³). The profile shape is assumed, not independently recovered.
Vertical mass column: (1500 m)q = 75,872.1 µg/m² = 75.8721 mg/m².
The reference is a baseline acquisition, not necessarily gas free air. Other species are assumed unchanged.
Saved CH₃CN example · numerical steps and sources in notes
03
Notes: The receiver senses an integrated path effect. It cannot independently estimate the concentration at every altitude from this one ray. Specifying an exponential shape reduces the unknown function to one scalar q. In the differential model q = 0 means no enhancement relative to the reference, not necessarily zero absolute CH3CN. The saved link budget treats baseline CH3CN attenuation as negligible. If the actual vertical shape is different, q remains a model dependent equivalent amplitude.
Equation source
\Delta c(z)=c_{\mathrm{sample}}(z)-c_{\mathrm{reference}}(z)=q\,e^{-z/(1500\ \mathrm m)}
Notation and units
q is the unknown surface equivalent increase (µg/m³). The profile shape is assumed, not independently recovered.
Conditions
The reference is a baseline acquisition, not necessarily gas free air. Other species are assumed unchanged.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 4
The fixed experiment used in all calculations
Parameter | Value
Geometry | 550 km LEO satellite, 90° ground elevation
Spectrum | 230–240 GHz, 1,024 tones; first tone 230.004883 GHz
Total RF power and apertures | 25 dBm; 0.10 m transmit / 1.0 m receive; η = 0.65
Noise and additional loss | 7 dB receiver noise figure; 5 dB implementation loss
Atmosphere and gas profile | ITU P.835 / P.676; CH₃CN scale height 1,500 m
Acquisition | 10 s reference + 10 s sample; 0.3% full pilot symbols
The static benchmark assumes ideal tracking. No source demonstrates this entire orbital configuration.
Saved CH₃CN example · numerical steps and sources in notes
04
Notes: LEO links are a useful example throughout the complete sensing chain. The same inference framework can use terrestrial or UAV geometry. The 25 dBm and 7 dB values have a published LEO design precedent in TeraLink, rather than flight validation. Aperture efficiency, implementation loss, vertical profile and calibration covariance are assumptions. Zenith is the shortest geometric path at a fixed orbit height; it cannot persist for a finite acquisition without time dependent tracking corrections.
Conditions
The static benchmark assumes ideal tracking. No source demonstrates this entire orbital configuration.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/54_supervisor_revision_2026_10_05.md
https://arxiv.org/html/2606.15410v1
https://www.itu.int/rec/R-REC-P.835-7-202408-I/en
https://www.itu.int/rec/R-REC-P.676-13-202208-I

## Slide 5
Step 1 · Mass concentration becomes molecular density
n₁: density for a numerical concentration of 1 µg/m³ · n(z;q): molecular density for the chosen q
41.053 g/mol: natural mixture molar mass · q is inserted numerically in µg/m³
At q = 50.5814, the surface molecular density is 7.419879e+17 molecules/m³.
HITRAN uses cm² per molecule, so the calculation converts density to cm⁻³ and path length to cm.
This converts an environmental concentration into the number of absorbers seen by the wave.
Saved CH₃CN example · numerical steps and sources in notes
05
Notes: The code uses concentration_ug_m3_to_number_density_cm3, giving 1.466918558936 × 10^10 molecules/cm³ per 1 µg/m³. Multiplying by q and exp(−z/1500) gives the molecular density at every integration node. This is dimensional conversion, not a fitted parameter. Natural molar mass is used for mass concentration; isotopologue mass is used for Doppler broadening. HITRAN intensity already contains natural isotope abundance, so the abundance is not applied a second time.
Equation source
\begin{gathered}n_1(0)=\frac{10^{-6}\ \mathrm{g/m^3}}{41.053\ \mathrm{g/mol}}\,(6.02214076\times10^{23})=1.46691856\times10^{16}\ \mathrm{m^{-3}}\\n(z;q)=q\,n_1(0)e^{-z/1500}\end{gathered}
Notation and units
n₁: density for a numerical concentration of 1 µg/m³ · n(z;q): molecular density for the chosen q
41.053 g/mol: natural mixture molar mass · q is inserted numerically in µg/m³
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json
https://hitran.org/docs/definitions-and-units/
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/src/thz_isac/concentration_units.py

## Slide 6
Step 2 · One actual HITRAN transition
Catalog parameter | Saved value | Physical role
Line center | 239.1379167 GHz | Transition frequency
S(296 K) | 2.616 × 10⁻²¹ cm/molecule | Integrated line strength
Air width γ_air | 0.1594 cm⁻¹/atm | Collision broadening
Lower state energy E″ | 47.8643 cm⁻¹ | Temperature dependence
Width temperature exponent | 0.71 | Temperature scaling of width
This is one of 17,880 retained CH₃CN transitions. The calculation sums their contributions.
The measured tone is at 230.004883 GHz. A transition contributes away from its center through its broadened shape.
Actual acquired HITRAN record · largest_line_contributions.csv
06
Notes: This is the largest individual contributor at the first tone and first altitude quadrature node, selected after evaluating all retained lines. It is not asserted to be the only relevant transition or a line centered on the tone. The molecule ID is 41 and local isotopologue ID is 1. The raw line wavenumber is 7.97678228 cm⁻¹, pressure shift is zero, and the actual record is exported with the derived contribution. Catalog range and line shape assumptions remain physical uncertainties.
Conditions
The measured tone is at 230.004883 GHz. A transition contributes away from its center through its broadened shape.
Sources
https://hitran.org/docs/definitions-and-units/
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/largest_line_contributions.csv

## Slide 7
Step 2 · A line shape gives absorption at our tone
At z = 16.8826 m | Value
Atmospheric state | T = 288.0403 K; p = 101,122.35 Pa
Temperature corrected strength S(T) | 2.845759 × 10⁻²¹ cm/molecule
Voigt value V at 230.004883 GHz | 0.4334214 cm
Sum over all retained lines: σ₀(z) | 2.642246 × 10⁻²⁰ cm²/molecule
σ_ℓ,₀: one transition’s absorption cross section at tone 0 · σ₀ = Σℓ σ_ℓ,₀
V is normalized over wavenumber. The temperature correction is worked out in the appendix.
σ is calculated from line parameters and atmospheric state. It is not a measured satellite attenuation.
Saved CH₃CN example · numerical steps and sources in notes
07
Notes: The Voigt function is the convolution of Doppler and collision broadening. Here the Lorentz half width is 0.1621900503 cm⁻¹ and the Doppler standard deviation is 6.42862709 × 10^−6 cm⁻¹. Their values are used at the actual tone wavenumber. Multiplying the temperature corrected line strength by this function gives one cross section. The other transitions supply the remaining sum. The layer has no single universal cross section: pressure and temperature change it with altitude.
Equation source
\sigma_{\ell,0}=S_\ell(T)V_\ell(f_0;T,p)=(2.845759\times10^{-21})(0.4334214)=1.233413\times10^{-21}\ \mathrm{cm^2}
Notation and units
σ_ℓ,₀: one transition’s absorption cross section at tone 0 · σ₀ = Σℓ σ_ℓ,₀
V is normalized over wavenumber. The temperature correction is worked out in the appendix.
Conditions
σ is calculated from line parameters and atmospheric state. It is not a measured satellite attenuation.
Sources
https://hitran.org/docs/definitions-and-units/
https://hitran.org/hapi/
https://www.itu.int/rec/R-REC-P.835-7-202408-I/en
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 8
Step 3 · The meaning of optical depth
Optical depth tells us how much absorption a wave accumulates along its path at a particular frequency.
Each thin layer contributes according to how many molecules it contains and how strongly they absorb. These contributions add along the path.
τ is dimensionless. The surviving power fraction is exp(−τ). At τ = 1, 36.8% survives and 63.2% is absorbed.
In this example, τ = 0.00280478: the extra gas absorbs 0.2801% of the power, giving a 0.1401% amplitude reduction.
Here τ describes the additional CH₃CN absorption. Geometric spreading and background losses are separate.
Saved CH₃CN example · numerical steps and sources in notes
08
Notes: Optical depth is the accumulated absorption coefficient along the ray: τ(f) = ∫ n(s) σ(f,s) ds. Its dimensions cancel because molecular density times absorption cross section is an inverse length. For a thin layer, dτ is approximately the fraction of the power entering that layer that it absorbs. Successive layers multiply their transmission factors, so their optical depths add. The exact total absorbed power fraction is 1 − exp(−τ), which is approximately τ only when τ is small. Optical refers to electromagnetic propagation here, including these radio frequencies. In this differential example, τ is the additional optical depth caused by the modeled enhancement relative to the reference, with other path effects matched. Power transmission is exp(−τ), whereas channel magnitude transmission is exp(−τ/2). For the saved first tone, τ = 0.002804781165 gives power transmission 0.997199148559 and amplitude transmission 0.998598592308. Atmospheric emission belongs to the separate background noise model.
Conditions
Here τ describes the additional CH₃CN absorption. Geometric spreading and background losses are separate.
Sources
https://hitran.org/docs/definitions-and-units/
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 9
Step 3 · One altitude node contributes optical depth
First quadrature node | Numerical value
Cross section σ₀ | 2.6422462 × 10⁻²⁰ cm²/molecule
Density n₁(z) for q = 1 µg/m³ | 1.4505008 × 10¹⁰ molecules/cm³
Integration weight w | 42.831123 m = 4,283.1123 cm
δτ₀,₁: dimensionless optical depth contribution at tone 0 for 1 µg/m³
The weight is a Gauss quadrature weight, not the thickness of a physical uniform slab.
Repeat this product at each altitude node and add the contributions.
Saved CH₃CN example · numerical steps and sources in notes
09
Notes: At zenith, the geometric path element equals the vertical element. The model uses order six Gauss quadrature over altitude intervals and inserts atmospheric layer boundaries, giving 114 nodes. The first node is at 16.882621449 m. Its number density is n1(0) exp(−16.882621449/1500). Its contribution in dB per unit q is 4.342944819 × 1.641537197735 × 10^−6 = 7.129105468153 × 10^−6. Numerical integration weights must not be interpreted as a measurement of the local gas profile.
Equation source
\delta\tau_{0,1}=\sigma_0n_1w=(2.6422462\times10^{-20})(1.4505008\times10^{10})(4283.1123)=1.6415372\times10^{-6}
Notation and units
δτ₀,₁: dimensionless optical depth contribution at tone 0 for 1 µg/m³
The weight is a Gauss quadrature weight, not the thickness of a physical uniform slab.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/quadrature_first_tone.csv

## Slide 10
Step 3 · Adding the atmosphere gives the tone sensitivity
Altitude interval | Optical depth for q = 1 µg/m³ | Attenuation sensitivity (dB per µg/m³)
0–0.5 km | 1.6389001e-05 | 7.1176528e-05
0.5–1 km | 1.1583791e-05 | 5.0307766e-05
1–2 km | 1.3936792e-05 | 6.0526719e-05
2–3 km | 6.9036665e-06 | 2.9982243e-05
3–5 km | 5.0671830e-06 | 2.2006496e-05
5–100 km | 1.5704107e-06 | 6.8202070e-06
Sum: τ₀,₁ = 5.5450845 × 10⁻⁵ → a₀ = (10 / ln 10) τ₀,₁ = 0.00024081996 dB/(µg/m³)
The vertical profile and atmospheric state determine this coefficient. It is not a universal CH₃CN constant.
Saved CH₃CN example · numerical steps and sources in notes
10
Notes: Each displayed row sums the exact quadrature contributions in that altitude interval, not a midpoint approximation. The 0–100 km total is 5.545084465494345 × 10^−5 optical depth per unit q. Multiplication by 10/ln10 gives 2.40819958505 × 10^−4 dB/(µg/m³), matching the earlier saved tone table to floating point precision. The full list of 114 nodes retains the temperature, pressure, cross section, molecular density and weight.
Conditions
The vertical profile and atmospheric state determine this coefficient. It is not a universal CH₃CN constant.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/altitude_contributions.csv

## Slide 11
Step 4 · The chosen concentration gives 0.012181 dB
ΔA₀: extra CH₃CN attenuation at the first tone · τ₀: corresponding dimensionless optical depth
The 4.5477 dB oxygen/water loss belongs to the baseline link budget.
The 0.012181 dB value is the additional loss caused by this CH₃CN enhancement.
The concentration multiplies a sensitivity computed from real spectral parameters and an assumed path profile.
Saved CH₃CN example · numerical steps and sources in notes
11
Notes: This is the missing multiplication behind the second row in the screenshot. Line strengths and cross sections determine a0, while q sets the magnitude of the extra gas column. This linearity is in optical depth and dB attenuation under the fixed trace gas line shape. The complex channel amplitude itself changes exponentially. Background cancellation assumes the reference and sample atmosphere are matched after correction.
Equation source
\begin{gathered}\Delta A_0=a_0q=(0.0002408199585)(50.5813966)=0.01218100983\ \mathrm{dB}\\\tau_0(q)=q\tau_{0,1}=(50.5813966)(5.545084465\times10^{-5})=0.002804781165\end{gathered}
Notation and units
ΔA₀: extra CH₃CN attenuation at the first tone · τ₀: corresponding dimensionless optical depth
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 12
Step 5 · Absorption predicts the amplitude change
h₀,₀: reference channel at tone 0 · h₁,₀: sample channel at tone 0, before measurement error
The ratio concerns channel magnitude after known geometric and instrument corrections.
The power ratio is 0.99719915. The stated 0.1401% is an amplitude reduction.
These are the third and fourth rows of the screenshot, now derived from the gas column.
A predicted change of 0.1401% is not yet evidence that a receiver can resolve it.
Saved CH₃CN example · numerical steps and sources in notes
12
Notes: Beer attenuation gives a power factor exp(−τ), hence an amplitude factor exp(−τ/2). The result is deterministic for the chosen concentration and physical model. It contains no receiver noise yet. The total received sample power at this tone becomes −97.61177776 dBm compared with the reference −97.59959675 dBm. The baseline channel magnitude is normalized to one for the next receiver calculation.
Equation source
\begin{gathered}\frac{|h_{1,0}|}{|h_{0,0}|}=e^{-\tau_0/2}=10^{-\Delta A_0/20}=10^{-0.01218100983/20}=0.9985985923\\100\left(1-\frac{|h_{1,0}|}{|h_{0,0}|}\right)=0.1401407692\%\end{gathered}
Notation and units
h₀,₀: reference channel at tone 0 · h₁,₀: sample channel at tone 0, before measurement error
Conditions
A predicted change of 0.1401% is not yet evidence that a receiver can resolve it.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://hitran.org/docs/definitions-and-units/

## Slide 13
Step 6 · Observation time fixes the averaging gain
Resource | Calculation
Tone spacing and useful symbol | 10 GHz / 1,024 = 9.765625 MHz; Tᵤ = 102.4 ns
Transmitted symbol | 102.4 ns + 10 ns assumed CP = 112.4 ns
Frame | 10,000 symbols, with 30 full pilot symbols
Frames in each 10 s acquisition | floor[10 / (10,000 × 112.4 ns)] = 8,896
Pilots per tone in each acquisition | M = 8,896 × 30 = 266,880
Both the reference and sample are noisy: 10 s + 10 s, not a free or exact reference.
Ideal phase, frequency, delay and gain tracking is assumed throughout each moving acquisition.
Saved CH₃CN example · numerical steps and sources in notes
13
Notes: This slide specifies the actual resources without teaching OFDM. The two schedules occupy 19.998208 seconds of complete frames, leaving 0.001792 seconds unused. A full pilot symbol measures all 1024 tones simultaneously. Sensing does not use the unknown payload symbols here. The 90 degree geometry is a snapshot approximation, and waiting for comparable reference conditions is additional operational time.
Conditions
Ideal phase, frequency, delay and gain tracking is assumed throughout each moving acquisition.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 14
Step 7 · One tone remains uncertain after averaging
First tone | Numerical value
Reference SNR per pilot, linear | ρ₀ = 0.961035658
Complex mean variance, normalized channel | 1 / (Mρ₀) = 3.8989213e-06
Thermal variance of the reference/sample log ratio | v₀(0) = 2.9415287e-04 dB²
Total null variance after calibration term | C₀₀ = 2.9515287e-04 dB²
C₀₀ = v₀(0) + (0.001 dB)² · The log ratio variance uses a high coherent mean SNR approximation.
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Saved CH₃CN example · numerical steps and sources in notes
14
Notes: The expected signal at this tone is 0.012181 dB, while the null standard deviation after both acquisitions is 0.017180 dB. Even with perfectly known gain this is not a reliable single tone detection. With an unknown gain offset, a single tone cannot distinguish attenuation from a gain change at all. The normalized real and imaginary noise components each have standard deviation 0.001396230873. Multiple frequencies are essential for both uncertainty reduction and separation from nuisance gain changes.
Equation source
v_0(0)=\frac{(20/\ln10)^2}{2M}\left(\frac1{\rho_0}+\frac1{\rho_0}\right),\qquad\sqrt{C_{00}}=0.0171800\ \mathrm{dB}
Notation and units
C₀₀ = v₀(0) + (0.001 dB)² · The log ratio variance uses a high coherent mean SNR approximation.
Conditions
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 15
Step 8 · The saved receiver draw does not equal its mean
Normalized complex pilot means, simulated | Value
Reference ĥ₀,₀ | 1.0009162403 + j 0.0004400251
Sample ĥ₁,₀ | 1.0007326946 − j 0.0009412581
Magnitudes ¦ĥ₀,₀¦ and ¦ĥ₁,₀¦ | 1.0009163371 and 1.0007331373
Persistent differential calibration draw e₀ | −0.0020537566 dB
The mean sample amplitude is 0.9985985923, but the noisy pilot mean can be larger. Seed: 20261005.
A positive gas enhancement can produce a negative observed attenuation at one noisy tone.
These are simulated complex observations with the stated noise and calibration model, not field measurements.
Saved CH₃CN example · numerical steps and sources in notes
15
Notes: Exactly replay the original random generator draw: z_r,k = (u+jv)/sqrt(2Mρ0,k), h0 = 1+z0 and h1 = 10^(−a q/20)+z1. The model then adds one correlated differential dB calibration draw per pair. Each displayed magnitude is calculated from both complex components. The final y0 equals the stored observation to numerical precision. This addresses the difference between the deterministic table and what a receiver could actually return.
Equation source
y_0=-20\log_{10}\!\left(\frac{1.0007331373}{1.0009163371}\right)-0.0020537566=0.0015899416-0.0020537566=-0.0004638149\ \mathrm{dB}
Notation and units
The mean sample amplitude is 0.9985985923, but the noisy pilot mean can be larger. Seed: 20261005.
Conditions
These are simulated complex observations with the stated noise and calibration model, not field measurements.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/complex_receiver_steps.csv

## Slide 16
Step 9 · The detector uses the complete observed spectrum
Chart: Differential attenuation (dB)
Input to estimation: y has 1,024 entries. The first is −0.0004638 dB, not the predicted +0.012181 dB.
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Saved CH₃CN example · numerical steps and sources in notes
16
Notes: All 1024 plotted observations are retained from the original saved simulation. The true template is shown for explanation, but the estimator does not receive q. It receives y, the template a calculated for one unit of concentration, a covariance model, and nuisance directions. Frequencies share a persistent correlated calibration error, so simply treating every sample as independent would overstate the information.
Conditions
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 17
Step 10 · The design matrix encodes gas and gain changes
Tone index k | aₖ [10⁻⁴ dB/(µg/m³)] | Offset column | Slope uₖ
0 | 2.408200 | 1 | -0.500000
255 | 2.804245 | 1 | -0.250733
511 | 4.032712 | 1 | -0.000489
767 | 6.489083 | 1 | 0.249756
1023 | 7.500802 | 1 | 0.500000
Five displayed rows are selected from all 1,024. uₖ = (fₖ − mean(f)) / (max(f) − min(f)).
b₀: common gain change (dB) · b₁: spectral gain slope coefficient (dB) · ε: remaining observation error (dB)
A contains known model responses. The unknowns are q and the two gain coefficients.
Saved CH₃CN example · numerical steps and sources in notes
17
Notes: The molecular column is generated by the same physical integration at every tone. The other columns permit a constant and linear spectral gain error. They stop these simple instrument changes from automatically being called gas. All three columns must be fitted jointly. The table scales only a by 10^4 for readability; calculations use unscaled a. Allowing more nuisance directions can reduce sensitivity further.
Equation source
\mathbf y=\mathbf A\boldsymbol\theta+\boldsymbol\varepsilon,\quad\mathbf A=[\mathbf a\ \mathbf1\ \mathbf u]\in\mathbb R^{1024\times3},\quad\boldsymbol\theta=[q\ b_0\ b_1]^T
Notation and units
Five displayed rows are selected from all 1,024. uₖ = (fₖ − mean(f)) / (max(f) − min(f)).
b₀: common gain change (dB) · b₁: spectral gain slope coefficient (dB) · ε: remaining observation error (dB)
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 18
Step 11 · The covariance encodes which errors average down
C is 1,024 × 1,024 in dB². Its thermal term includes reference and sample noise.
10⁻⁶ dB² is the assumed differential calibration variance; it is not divided by M.
For example: C₀₀ = 2.95152865 × 10⁻⁴ dB², while C₀,₁₀₂₃ = 3.68238874 × 10⁻⁷ dB².
The estimator fixes its weights using C(0). Detection probability at q > 0 uses the corresponding C(q).
The calibration covariance is an explicit unmeasured assumption, not an estimate obtained from these data.
Saved CH₃CN example · numerical steps and sources in notes
18
Notes: The residual describes the reference/sample difference, so it is added once, not once for each acquisition. The null covariance assumes the two per pilot SNR values are equal. Under a positive enhancement the sample is weaker, slightly increasing its variance. The actual log amplitude observations are not exactly Gaussian; the high coherent mean SNR supports the delta approximation and the saved Monte Carlo control checks it within the model.
Equation source
\begin{gathered}\mathbf C(q)=\operatorname{diag}(v_k(q))+10^{-6}\mathbf R,\qquad R_{ij}=e^{-|f_i-f_j|/(10\ \mathrm{GHz})}\\v_k(q)=\frac{(20/\ln10)^2}{2M}\left[\rho_{0,k}^{-1}+\rho_{1,k}(q)^{-1}\right],\quad\rho_{1,k}(q)=\rho_{0,k}10^{-a_kq/10}\end{gathered}
Notation and units
C is 1,024 × 1,024 in dB². Its thermal term includes reference and sample noise.
10⁻⁶ dB² is the assumed differential calibration variance; it is not divided by M.
Conditions
The calibration covariance is an explicit unmeasured assumption, not an estimate obtained from these data.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 19
Step 12 · Weighted regression estimates the unknowns
G = Aᵀ C(0)⁻¹ A, a 3 × 3 matrix · g = Aᵀ C(0)⁻¹ y, a 3 × 1 vector
θ̂ = [q̂, b̂₀, b̂₁]ᵀ · C(0)⁻¹ accounts for unequal noise and cross frequency correlation
The fit seeks the concentration whose spectral shape best explains y after allowing gain offset and slope.
The next slide gives every entry of the resulting three dimensional system.
The receiver does not divide each observed tone by aₖ and average the answers.
Saved CH₃CN example · numerical steps and sources in notes
19
Notes: This is generalized least squares under the stated covariance. The saved production estimator uses Cholesky solves and SVD projection, avoiding explicit inverses. The worked replay computes G and g using Cholesky solves and solves the small system. Its q agrees with the original estimator H y. The normal equations are shown because they expose every coefficient in a compact numerical example, not because explicit matrix inversion is recommended.
Equation source
\widehat{\boldsymbol\theta}=\arg\min_{\boldsymbol\theta}(\mathbf y-\mathbf A\boldsymbol\theta)^T\mathbf C(0)^{-1}(\mathbf y-\mathbf A\boldsymbol\theta),\qquad\mathbf G\widehat{\boldsymbol\theta}=\mathbf g
Notation and units
G = Aᵀ C(0)⁻¹ A, a 3 × 3 matrix · g = Aᵀ C(0)⁻¹ y, a 3 × 1 vector
θ̂ = [q̂, b̂₀, b̂₁]ᵀ · C(0)⁻¹ accounts for unequal noise and cross frequency correlation
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 20
Step 12 · The full spectrum reduces to this numerical system
Equation row | Coefficient of q | Coefficient of b₀ | Coefficient of b₁ | Right side g
1 | 0.301344020 | 458.463514 | 127.082723 | 15.066265191
2 | 458.463513671 | 983654.579709 | -223.779287 | 22141.401031152
3 | 127.082722926 | -223.779287 | 198502.414349 | 7023.360955313
The matrix columns correspond to different parameter units: q in µg/m³, b₀ and b₁ in dB.
All values use all 1,024 tones. Displayed coefficients are rounded; source arrays retain full precision.
The small q coefficient alone is not the usable information: much of the gas pattern resembles gain changes.
Saved CH₃CN example · numerical steps and sources in notes
20
Notes: Use the displayed system to reproduce the estimate, allowing for rounded coefficients. The full precision G, g and theta are saved in normal_equations.npz and worked_steps.json. The effective information is Gqq − Gqb Gbb^−1 Gbq, which is much smaller than Gqq. A and C are both necessary to construct this system; y appears only in g.
Equation source
\begin{bmatrix}G_{qq}&\mathbf G_{qb}\\\mathbf G_{bq}&\mathbf G_{bb}\end{bmatrix}\begin{bmatrix}\widehat q\\\widehat{\mathbf b}\end{bmatrix}=\begin{bmatrix}g_q\\\mathbf g_b\end{bmatrix}
Notation and units
The matrix columns correspond to different parameter units: q in µg/m³, b₀ and b₁ in dB.
All values use all 1,024 tones. Displayed coefficients are rounded; source arrays retain full precision.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/normal_equations.npz

## Slide 21
Step 13 · Eliminating gain terms gives the concentration
I_q: information for q after removing the gain nuisance terms [(µg/m³)⁻²]
t_q: remaining weighted evidence for q [(µg/m³)⁻¹]
The same solve gives b̂₀ = 0.00413651 dB and b̂₁ = 0.01014643 dB.
The true simulated q was 50.5814 µg/m³. The estimate is different because this observation contains error.
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Saved CH₃CN example · numerical steps and sources in notes
21
Notes: This is the scalar Schur complement of the two gain parameters. It is algebraically equivalent to the whiten and project construction in the source tutorial. The subtraction removes the component of the molecular column that can be explained by a constant and a spectral slope. Rounding the two terms too aggressively before subtraction can lose precision, so the script uses full precision throughout. The inferred b coefficients are fitted nuisance values; they are not independent instrument calibration measurements.
Equation source
\begin{gathered}I_q=G_{qq}-\mathbf G_{qb}\mathbf G_{bb}^{-1}\mathbf G_{bq}=0.3013440205-0.2951744347=0.006169585805\\t_q=g_q-\mathbf G_{qb}\mathbf G_{bb}^{-1}\mathbf g_b=15.0662651908-14.8230312721=0.243233918673\\\widehat q=t_q/I_q=39.42467555\ \mathrm{\mu g/m^3}\end{gathered}
Notation and units
I_q: information for q after removing the gain nuisance terms [(µg/m³)⁻²]
t_q: remaining weighted evidence for q [(µg/m³)⁻¹]
Conditions
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 22
Step 14 · The estimate exceeds a prespecified threshold
H₀: q = 0 · H₁: q > 0 · s₀: standard deviation under H₀
q_th: threshold for 1% false alarm probability for this one prespecified compound and decision
The decision says the observed pattern is inconsistent with no enhancement under this model.
It does not establish exact concentration, unique chemical identity in a changing mixture, or field performance.
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Saved CH₃CN example · numerical steps and sources in notes
22
Notes: The threshold is fixed from the null model before inspecting the observation. The unconstrained signed estimator is used for the test; truncating negative estimates to zero would change its null distribution. This one successful random draw does not itself show 95% detection probability. The threshold and a 95% power concentration are different quantities.
Equation source
\begin{gathered}s_0=I_q^{-1/2}=12.73127783\ \mathrm{\mu g/m^3}\\q_{\mathrm{th}}=z_{0.99}s_0=(2.326347874)(12.73127783)=29.61738111\ \mathrm{\mu g/m^3}\\\widehat q=39.42467555>29.61738111\quad\Longrightarrow\quad\text{detection}\end{gathered}
Notation and units
H₀: q = 0 · H₁: q > 0 · s₀: standard deviation under H₀
q_th: threshold for 1% false alarm probability for this one prespecified compound and decision
Conditions
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 23
Why the chosen q was 50.5814 µg/m³
s₁(q) = √[H C(q) Hᵀ] · H is the first row of G⁻¹ Aᵀ C(0)⁻¹, so q̂ = H y.
z₀.₉₅: standard normal 95th percentile · these weights are fixed under the null.
This concentration was selected from the analytical sensitivity calculation before the random receiver draw.
It is a controlled simulation input. It was neither measured in the atmosphere nor estimated from the sample.
The threshold is 29.6174 µg/m³. Achieving 95% predicted response requires a larger true enhancement.
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Saved CH₃CN example · numerical steps and sources in notes
23
Notes: The equation is implicit because s1 depends slightly on q through sample SNR. The code solves it numerically; evaluating at its solution gives the arithmetic displayed here. The constant variance approximation would give 50.5585 µg/m³. This explains the otherwise arbitrary looking number in the screenshot. It does not imply this is an environmentally typical concentration.
Equation source
\begin{gathered}\Pr(\widehat q>q_{\mathrm{th}}\mid q)=0.95\quad\Longleftrightarrow\quad q-q_{\mathrm{th}}=z_{0.95}s_1(q)\\q_{95}=29.61738111+(1.644853627)(12.74521644)=50.58139660\ \mathrm{\mu g/m^3}\end{gathered}
Notation and units
s₁(q) = √[H C(q) Hᵀ] · H is the first row of G⁻¹ Aᵀ C(0)⁻¹, so q̂ = H y.
z₀.₉₅: standard normal 95th percentile · these weights are fixed under the null.
Conditions
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 24
Repeated observations show success and failure rates
10,000 simulated reference/sample pairs at each concentration, using the same fixed threshold.
True q (µg/m³) | Predicted response | Simulated response | 95% interval
0 | 1.00% | 1.13% | 0.93–1.36%
1 | 1.23% | 1.31% | 1.10–1.55%
50.5814 | 95.00% | 94.75% | 94.29–95.18%
1 µg/m³ is not reliably detected: the simulated response is only 1.31%, near the false alarm rate.
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Saved CH₃CN example · numerical steps and sources in notes
24
Notes: The counts are 113/10000 under q=0, 131/10000 at q=1 and 9475/10000 at q=50.5814. The exact binomial intervals describe Monte Carlo uncertainty, not uncertainty in hardware calibration, spectroscopy or real weather. The observations use complex pilot means, rather than directly drawing a Gaussian concentration estimate.
Conditions
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/results/zenith_single_compound/receiver_control.csv

## Slide 25
What is real, assumed and simulated in this example
Evidence category | What belongs to it
External physical inputs | Actual HITRAN records; published ITU atmospheric models
Design assumptions | 550 km geometry; hardware configuration; exponential gas enhancement
Unmeasured error assumption | 0.001 dB differential residual and its spectral covariance
Simulated observation | Complex pilot means, calibration draw and resulting y
Not demonstrated | Measured atmospheric detection, ambient sensitivity or 3D reconstruction
The calculation is concrete and reproducible. It is not an orbital measurement.
A selected aircraft background reference is about 0.252 µg/m³, far below this conditional enhancement limit.
Saved CH₃CN example · numerical steps and sources in notes
25
Notes: The EMeRGe/IAGOS contextual reference is 145 pptv, equivalent to about 0.252 µg/m³ at 288.15 K and 101325 Pa. It is not a universal ground concentration or a concentration profile measurement for this example. Real detection requires independently measured concentration, blank stability and a tested moving receiver. Multiple ground receivers would require adequate ray diversity and an identifiable tomographic model. LEO is a useful example for the full chain, not evidence that every proposed sensing mode is feasible.
Conditions
A selected aircraft background reference is about 0.252 µg/m³, far below this conditional enhancement limit.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/54_supervisor_revision_2026_10_05.md
https://acp.copernicus.org/articles/23/1893/2023/index.html

## Slide 26
The original table, now with its calculation attached
Quantity | How the value is obtained | Result
Chosen enhancement | Solve the 95% power equation, then set the simulation input | 50.5814 µg/m³
Extra absorption at tone 0 | (0.0002408199585) × 50.5813966 | 0.012181 dB
Sample/reference amplitude | 10^(−0.01218100983 / 20) | 0.998599
Amplitude reduction | 100 × (1 − 0.9985985923) | 0.1401%
After adding the modeled errors and fitting all tones: q̂ = 39.4247 µg/m³ > threshold 29.6174 → detection.
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Saved CH₃CN example · numerical steps and sources in notes
26
Notes: This closes the requested explanation of the screenshot. The deterministic chain and statistical inverse are different operations. The forward model computes a pattern from a chosen concentration; the receiver fit estimates concentration from noisy observations without knowing the chosen value. That distinction is necessary to avoid confusing the simulated truth, predicted attenuation and retrieved concentration.
Conditions
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 27
Appendix · Temperature correction for the actual line
Q(T): molecular partition sum · E″ = 47.8643 cm⁻¹ · ν̃ = 7.97678228 cm⁻¹
c₂: second radiation constant (cm K) · T = 288.040263 K
Q(296) / Q(T) = 88658.97016 / 83172.06723 = 1.065970501.
S(T) = 2.616 × 10⁻²¹ × 1.065970501 × 0.993591393 × 1.027087331 = 2.845759 × 10⁻²¹ cm/molecule.
The line strength changes with state populations and stimulated emission before the profile is applied.
Saved CH₃CN example · numerical steps and sources in notes
27
Notes: The partition sums come from HAPI TIPS2025. The Boltzmann factor uses the lower state energy, and the last factor corrects stimulated emission. Width is also adjusted: γ = 0.1594 × (101122.3515/101325) × (296/288.040263)^0.71 = 0.1621900503 cm⁻¹. The saved source uses the second radiation constant defined in physical_spectroscopy.py. All factors are calculated at the first actual quadrature node, not at a rounded atmospheric state.
Equation source
S(T)=S(296)\frac{Q(296)}{Q(T)}\exp\!\left[-c_2E^{\prime\prime}\left(\frac1T-\frac1{296}\right)\right]\frac{1-e^{-c_2\widetilde\nu/T}}{1-e^{-c_2\widetilde\nu/296}}
Notation and units
Q(T): molecular partition sum · E″ = 47.8643 cm⁻¹ · ν̃ = 7.97678228 cm⁻¹
c₂: second radiation constant (cm K) · T = 288.040263 K
Sources
https://hitran.org/docs/definitions-and-units/
https://hitran.org/hapi/
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 28
Appendix · Power and noise at the first tone
Link budget term | Value
Transmit power per tone | 25 − 10 log₁₀(1024) = −5.1030 dBm
Transmit + receive gains | 45.7705 + 65.7705 dBi
Free space + background + implementation loss | 194.4898 + 4.5477 + 5.0000 dB
Reference / sample received power | −97.5996 / −97.6118 dBm
Noise power in one tone | −97.4270 dBm
Reference per pilot SNR | −0.172605 dB = 0.96103566 linear
The extra 0.012181 dB CH₃CN loss belongs only to the sample in this enhancement model.
Saved CH₃CN example · numerical steps and sources in notes
28
Notes: Received power equals per tone power plus both antenna gains minus free space, background and implementation loss. Noise uses kB(Tsky+Te)Δf, with Tsky = 177.831 K and Te = 290(10^(7/10)−1). The noise figure is not counted twice. More exact values are saved in tone_by_tone.csv. The 25 dBm is the total average RF power across all tones, not per tone or electrical input power.
Conditions
The extra 0.012181 dB CH₃CN loss belongs only to the sample in this enhancement model.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://www.itu.int/rec/R-REC-P.676-13-202208-I
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/results/zenith_single_compound/tone_by_tone.csv

## Slide 29
Appendix · Five actual rows of the covariance
This is a submatrix of the full null covariance, not a new error model.
C / 10⁻⁴ dB² | 0 | 255 | 511 | 767 | 1023
0 | 2.951529 | 0.007796 | 0.006071 | 0.004728 | 0.003682
255 | 0.007796 | 2.947224 | 0.007788 | 0.006065 | 0.004724
511 | 0.006071 | 0.007788 | 2.947702 | 0.007788 | 0.006065
767 | 0.004728 | 0.006065 | 0.007788 | 2.952581 | 0.007788
1023 | 0.003682 | 0.004724 | 0.006065 | 0.007788 | 2.961572
The off diagonal elements carry the assumed correlation between spectral errors.
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Saved CH₃CN example · numerical steps and sources in notes
29
Notes: Each row and column is indexed by the original tone number. Multiply each displayed entry by 10^−4 dB² to obtain the covariance value. The diagonal includes both thermal and persistent calibration variance. Selecting only these tones requires recalculating the estimator using the corresponding A rows and this submatrix. Taking five entries from the full H would not produce the five tone estimator.
Conditions
20 s total • ideal tracking • assumed, unmeasured 0.001 dB differential calibration residual
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 30
Appendix · A five tone dot product can be checked by hand
Tone k | Observed yₖ (dB) | Five tone weight H₅,ₖ | Product H₅,ₖ yₖ
0 | -0.000463815 | 4942.686 | -2.292492
255 | 0.025099503 | -4201.176 | -105.447434
511 | -0.031417175 | -5681.920 | 178.509866
767 | 0.018701897 | 4215.931 | 78.845915
1023 | 0.030551022 | 724.479 | 22.133560
Sum = 171.7494 µg/m³; standard deviation = 165.1163; threshold = 384.1179 → no detection.
This discards 1,019 tones. The main detector uses all 1,024, with the same assumed 0.001 dB residual and 20 s total.
Saved CH₃CN example · numerical steps and sources in notes
30
Notes: These are the same five observations extracted from the full simulated spectrum. The weights are recomputed for only these five tones while allowing the same gain offset and slope. The entries and their products show a literal matrix multiplication. Its large uncertainty means the estimate 171.7494 is not persuasive evidence, even though it is larger than the full spectrum estimate. Source values retain full precision; the displayed products use full precision before rounding.
Conditions
This discards 1,019 tones. The main detector uses all 1,024, with the same assumed 0.001 dB residual and 20 s total.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json

## Slide 31
Appendix · Hardware evidence keeps its original scope
Source | Useful evidence | What it does not establish
Sen et al., Nature Electronics | 200 mW at 210–240 GHz, terrestrial link | Orbital operation
TeraLink, 2026 preprint | 25 dBm, 7 dB NF, proposed LEO system | Flight validation of this example
Cooper et al., JMW | >400 mW CW at 240 GHz | A complete 10 GHz OFDM modem
The selected parameters have physical references, but combined bandwidth, calibration and tracking remain unverified.
1 W and 10 W transmit cases elsewhere in the repository are sensitivity scenarios, not qualified payload specifications.
Primary hardware references · exact URLs in notes
31
Notes: Transmit power values must refer to the same quantity when comparing hardware: average linear OFDM output differs from peak pulse power and electrical supply power. The published design and laboratory references are meaningful anchors but cannot prove the whole assumed measurement chain. The research note retains antenna dimensions, pointing, surface tolerance, motion and power comparisons.
Conditions
1 W and 10 W transmit cases elsewhere in the repository are sensitivity scenarios, not qualified payload specifications.
Sources
https://www.nature.com/articles/s41928-022-00897-6
https://arxiv.org/html/2606.15410v1
https://doi.org/10.1109/JMW.2025.3610360
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/54_supervisor_revision_2026_10_05.md

## Slide 32
Sources · Spectroscopy and atmospheric state
HITRAN: actual CH₃CN line records, units, temperature correction and absorption model. hitran.org/docs/definitions-and-units/
HAPI and TIPS2025: partition functions used in the spectral calculation. Kochanov et al., JQSRT 177 (2016), DOI 10.1016/j.jqsrt.2016.03.005.
ITU P.835-7 (2024): standard atmospheric state. ITU P.676-13 (2022): oxygen/water propagation and emission.
EMeRGe / IAGOS context: ACP 23, 1893 (2023), DOI 10.5194/acp-23-1893-2023.
Primary sources · clickable URLs in notes
32
Notes: These are primary method and context references. The HITRAN table is an external physical input; the code adds the declared geometry, concentration profile and receiver error assumptions. See the linked source audit for each claim boundary. HAPI version in the retained experiment is 1.3.0.0.
Sources
https://hitran.org/docs/definitions-and-units/
https://hitran.org/hapi/
https://www.itu.int/rec/R-REC-P.835-7-202408-I/en
https://www.itu.int/rec/R-REC-P.676-13-202208-I
https://acp.copernicus.org/articles/23/1893/2023/index.html

## Slide 33
Sources · Every numerical step is saved
worked_steps.json contains the values substituted in the equations.
quadrature_first_tone.csv and altitude_contributions.csv expose the complete atmospheric integral.
complex_receiver_steps.csv records both complex pilot means and the final observation at every tone.
normal_equations.npz stores G, g and θ̂; the original matrices.npz contains the full A, C and H.
Reproduce with scripts/calculate_zenith_worked_steps.py. The saved source hashes are in manifest.json.
Saved CH₃CN example · numerical steps and sources in notes
33
Notes: The numerical replay starts from the original experiment snapshot b94f3fe and does not alter the main scientific result. The data directory is results/zenith_worked_steps. The physical forward sum and the complex random draw are independently replayed, then compared against the saved outputs. The first tone sensitivity, whole spectrum estimate and uncertainty agree. Equations and slide source values are drawn from these files.
Sources
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/worked_steps.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/results/zenith_worked_steps/manifest.json
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/main/scripts/calculate_zenith_worked_steps.py
https://github.com/unworthyzeus/THz_ISAC_atmospheric_monitoring/blob/b94f3fe/docs/55_zenith_single_compound_walkthrough.md